## Slide 1
An Evaluation of Biological and Chemical Improvements at Various Spatial Scales in the West Branch Susquehanna River Watershed, Pennsylvania
Shawn Rummel
Lead Science Advisor
Trout Unlimited, Northeast Coldwater Habitat Program
Coauthors: Amy Wolfe, Rachel Kester, Kathleen Lavelle, and Allison Lutz

## Slide 2: West Branch Susquehanna River Watershed
12,090 miles of streams within subbasin
  Warm and coldwater fisheries
5,070 miles support natural trout reproduction (42%)
  1,090 miles of Class A Trout water (>30 kg/ha)
Approx. 50% of watershed area is public (state forest or state parks)

## Slide 3: West Branch Susquehanna River Watershed
12,090 miles of streams within subbasin
  Warm and coldwater fisheries
5,070 miles support natural trout reproduction (42%)
  1,090 miles of Class A Trout water (>30 kg/ha)
Approx. 50% of watershed area is public (state forest or state parks)
1,200 miles of AMD impaired waters (PA DEP)

## Slide 4: Impact of AMD on Aquatic Ecosystems
Water Quality
  Decreased pH
  Increased metal concentrations: Fe, Al, Mn, etc.
Habitat
  Increased sedimentation to streams from abandoned mine lands
  Precipitating metals often coat substrate (limits benthic macroinvertebrate habitat and fish spawning habitat)
Benthic Macroinvertebrates & Fish
  Loss of pollution sensitive taxa
  Decreased growth, reproduction, or death
  Increased avoidance behavior or movements for mobile organisms
  Dissolved metals are toxic to aquatic life
  High metal concentrations interrupt respiration in aquatic organisms
  Isolation of populations due to water quality barrier

## Slide 5: Kettle Creek Watershed
90% watershed, 224 sq mi, is designated as Exceptional Value water quality (largest in PA)
Kettle Creek mainstem is one of PA’s most heavily fished stocked trout streams, while tributaries contain some of PA’s most well known native brook trout streams
Although completely underlain by Marcellus shale, majority of watershed aside from very headwaters will not be developed due to natural gas storage deep wells in the Oriskany sandstone

## Slide 6: Kettle Creek Watershed AMD
Unfortunately 12 miles AMD pollution and 1,087 acres of abandoned mines in lower section of watershed
Deep and surface mines in the Upper and Lower Kittanning coal seams
pH 2.5 – 3.5
Acidity 200 – 600 mg/L
Fe 20 – 50 mg/L
Al 20 – 70 mg/L

## Slide 7: Kettle Creek Restoration Projects (Since 2004)

## Slide 8: Middle Branch Fishery Survey Data
Chart: Density (brook trout per hectare)
| 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | UPS (Mean)
Density (brook trout per ha) | 0 | 20 | 131 | 470 | 1691 | 1792 | 885 | 1235
No Data
No Data
Chart: Number of 25 mm Size Classes
| 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | UPS
Number of 25 mm Size Classes | 0 | 1 | 4 | 6 | 7 | 6 | 5 | 5
No Data
No Data

## Slide 9: Benthic Macroinvertebrate Biological Metrics – Middle Branch
No Data
PA IBI Scores
 | DWS Treatment |  |  |  |  |  |  | UPS Mean
 | 2008 | 2010 | 2012 | 2013 | 2014 | 2015 | 2017 | 
Total Taxa Richness | 3 | 7 | 15 | 21 | 27 | 14 | 10 | 19.5
EPT Taxa Richness | 1 | 6 | 8 | 9 | 13 | 7 | 6 | 10
% Sensitive Individuals | 33.3 | 97.8 | 55.6 | 40.0 | 61.0 | 69.8 | 80.3 | 55.7

## Slide 10: Functional Feeding Groups
Collector-Gatherers (CG)
  Collect Fine Particulate Organic Matter (FPOM)from stream bottom
Filterers-Collectors (FC)
  Collect FPOM from water column using filters
Predators (PR)
  Feed on other consumers
Scrapers (SC)
  Consume algae and associated material
Shredders (SH)
  Consume leaf litter and coarse organic matter

## Slide 11: Resiliency of AMD Restored Systems?
IBI = 57
Taxa Richness = 22
% Sensitive = 31.8%
October 2016 – High Flow Event
pH = 3.4
Alk = 0 mg/L
Acid = 122 mg/L
Al = 13.5 mg/L
No Brook Trout found in surveys following event
IBI = 27.7
Taxa Richness = 10
% Sensitive = 4.3%
Modest Brook Trout population present in Fall 2017 Surveys of Twomile Run

## Slide 12: West Branch Susquehanna River Watershed
12,090 miles of streams within subbasin
  Warm and coldwater fisheries
5,070 miles support natural trout reproduction (42%)
  1,090 miles of Class A Trout water (>30 kg/ha)
Approx. 50% of watershed area is public (state forest or state parks)
1,200 miles of AMD impaired waters (PA DEP)

## Slide 13: AMD Treatment Systems and Reclamation Projects
Approximately 80 treatment sites throughout the West Branch
What impact are they having at a large scale?
Prior to 2009, last comprehensive water quality survey of the watershed was completed in the 1970’s

## Slide 14: West Branch Susquehanna Recovery Benchmark II (2017-2019)
Objectives:
  Replicate 2009 study; expand to 109 sample sites including reference sites
  Prioritization of future projects
  Establish long-term monitoring strategy for West Branch
  Develop citizen science AMD monitoring guide
How has treatment impacted the watershed?
Can benthic macros be used as a measure of success?
Threshold criteria for restoration success?
Timeline for recovery?

## Slide 15: Water Chemistry – Change between 2009 & 2017; Low Flow Samples
pH
Dissolved Al
Mean Low flow pH: 2009 = 5.18; 2017= 5.46
Range = 2.8 - 8.0

## Slide 16: Benthic Macroinvertebrate Preliminary Results
Biological Metric (Mean) | 2009 | 2017 | Reference
Total Individuals | 35.24 | 103.59 | 206.63
Taxa Richness | 7.93 | 18.20 | 35.34
EPT Taxa Richness | 2.18 | 4.76 | 16.77
Beck’s Index | 4.43 | 9.16 | 32.91
Hillsenhoff Index | 4.60 | 4.71 | 2.68
Shannon Diversity Index | 1.44 | 2.13 | 2.73
IBI | 33.02 | 44.86 | 86.10

## Slide 17: Functional Feeding Groups
Collector-Gatherers (CG)
  Collect Fine Particulate Organic Matter (FPOM)from stream bottom
Filterers-Collectors (FC)
  Collect FPOM from water column using filters
Predators (PR)
  Feed on other consumers
Scrapers (SC)
  Consume algae and associated material
Shredders (SH)
  Consume leaf litter and coarse organic matter

## Slide 18: Fishery Response
Surveys to be completed on the mainstem of river in Summer 2019
Since 2010, fishery surveys have documented 401 miles of wild trout streams in the watershed, an increase of 216 miles.
27.8 miles of the mainstem West Branch Susquehanna River now supports wild trout – downstream of an active treatment system
  This section is now managed as catch & release.

## Slide 19: Next Steps
Compile monitoring data on treatment systems – determine capacity of treatment
Quantify chemical and biological improvements in watershed due to treatment
Analyze aquatic community composition across environmental gradient – water quality, habitat, land use, etc.
  Thresholds in community metrics and/or taxa to help guide restoration objectives and goals
  Can macroinvertebrates and/or fishery communities be used to assess progress/success of restoration along gradient?
Establish a general timeline for recovery of AMD streams from sites with long-term monitoring
  How long until restoration sites mimic reference sites?
Establish a probabilistic long-term monitoring strategy for the West Branch Susquehanna River watershed

## Slide 20
Shawn Rummel
Lead Science Advisor
Northeast Coldwater Habitat Program
Lock Haven, PA
shawn.rummel@tu.org
814-360-2633
Thank you!