## Slide 1
Presented to:
2019 ASMR National Meeting of the American Society of Mining and Reclamation
Presented:
June 3-6, 2019 Big Sky, Montana
Presented by:
Pioneer Technical Services, Inc.
Reclamation of the McLaren Tailings
The Rest of the Story

## Slide 2: Presentation Outline
Project Settings
History
Challenges
Construction
Post Reclamation

## Slide 3: McLaren – Cooke City Montana
McLaren Tailings Site

## Slide 4: Project Setting
Cooke City
McLaren Tailings
Yellowstone National Park
Notes: 4

## Slide 5: McLaren Mill and Tailings
McLaren Tailings
Soda Butte Creek
Miller Creek
McLaren Mill Site
Notes: 5

## Slide 6: Approximate Pre-Mining Creek Locations
Pre-mining Soda Butte Creek (approximate)
Pre-mining Miller Creek
(approximate)
Notes: 6

## Slide 7: HISTORY
New World Mining District
  Near Cooke City and Northwest Entrance to Yellowstone National Park
  Site of Crown Butte $65M Buyout in 1997 and USFS $30M Cleanup
  McLaren Mill
  Processed Gold and Copper ore from 1933 – 1953
  Produces 60,000 troy oz of gold, 2,000 short tons of copper
  Tailings Impoundment grew over Soda Butte Creek and Miller Creek
  1950 tailings release mapped to the Lamar River
Notes: Walter McLaren invented the ice cream cone

## Slide 8: WHY

## Slide 9: Seep from Toe of Dam

## Slide 10: Soda Butte Creek Below Tailings
Tailings Discharges (USGS):
Fe 418 mg/L
Al 122 mg/L
Cu 6 mg/L
Pb 0.6 mg/L
Cd 0.06 mg/L
Approximate Annual Loads:
40,000 lb Fe
12,000 lb Al
590 lb Cu
58 lb Pb
6 lb Cd
No Color Enhancement
Notes: 10

## Slide 11: Soda Butte Creek Below Tailings No Color Enhancement

## Slide 12: McLaren Reclamation Challenges
Dewater the tailings by pumping the underlying aquifer
  Intercept clean water
  Treat contaminated water to DEQ water quality standards

## Slide 13: McLaren Reclamation Challenges
Saturated tailings up to 50% moisture
Stabilize tailings using quick Lime (3 to 5%)
Reduce metal mobility

## Slide 14: Sometimes Just Getting There

## Slide 15: GROUNDWATER
  Groundwater fluctuation 12-15 feet
  To effectively dewater the site would require 17 wells
  Pumping up to 500 gallons per minute
  Groundwater from 8 of the wells would require treatment (primarily pH, Cu, Fe, Mg and Al)

## Slide 16
Final Pumping Well Design Locations
Capture of Impacted Groundwater Using Interior Wells
Capture of Clean Groundwater Using Perimeter Wells

## Slide 17: Start of Construction 2010
Knife River – Yellowstone Division, Billings, Montana. Mobilized to the Site June 2, 2010
  Install BMPs
  Install west and east bridges
  Construct Water Treatment Building (WTB)
  Clear, Grub and partial excavation of repository area
  Stabilization of 10,990 cubic yards of tailings
Notes: Out of 50 contractors at pre-bid 10/28/2009 only 3 bid on project KR, Ofteldal and Shumaker

## Slide 18: Construction 2010

## Slide 19: Construction 2010

## Slide 20: Construction 2011
KR started summer construction June 13, 2011
Completed WTB (electrical, plumbing, wiring of wells)
Complete excavation of Repository 24,000 cy
Salvaged 13,000 cy of cover soil
DEWATER, DEWATER, and DEWATER
Stabilized and placed 55,900 cy of tailings
Constructed sediment detention pond

## Slide 21: Construction 2011

## Slide 22: Construction 2011

## Slide 23: Construction 2011
Cu and Fe > 1000x DEQ-7
Pb > 100x DEQ-7
Cd, Ag, As, Zn > 10x DEQ-7
1-5 million gallons water
30 feet of tailings

## Slide 24: Construction 2011

## Slide 25: Construction 2011

## Slide 26: RCTS

## Slide 27: Construction 2011
Summer construction shut down October 20, 2011

## Slide 28: Construction 2012
Summer Construction started on May 17, 2012
Stabilized 169,000 cy tailings
Excavated, stockpiled 46,700 cy cover soils
Installed 25,475 sq yd of temporary liner over compacted tailings in the repository
Used 8,930 tons of quick lime
Used 5 drums of anionic flocculant

## Slide 29: Construction 2012

## Slide 30: Construction 2012

## Slide 31: Construction 2012

## Slide 32: Construction 2012

## Slide 33: Construction 2012

## Slide 34: Construction 2012

## Slide 35: Construction 2012

## Slide 36: Construction 2012

## Slide 37: Construction 2013 Highlights
Stabilized 29,100 cy of tailings
Excavated and stockpiled 12,000 cy of cover soil
Removed 17 pumping wells
Removed the WTB
Constructed 1,315 feet of Soda Butte Creek
Constructed 465 feet of Miller Creek
Installed 25,595 sq yds of geocushion and HDPE liner at repository

## Slide 38: Construction 2013

## Slide 39: Construction 2013

## Slide 40: Construction 2013

## Slide 41: Construction 2013

## Slide 42: Construction 2013
Notes: Turned Soda Butte Creek into new on August 30th

## Slide 43: Construction 2013
Notes: Geocushion and 60 mil HDPE

## Slide 44: Construction 2013
October 2nd

## Slide 45: Construction 2013
October 3rd ~8” of snow

## Slide 46: Construction 2013
October 13th

## Slide 47: Construction 2014 Highlights
Started June 5
Mixed 4,360 dry tons of compost with cover soil for a target of 3% organic matter (volume basis)
Backfilled 35,400 cy of amended cover soil
Installed 23800 sq yds of geonet on repository
Placed 28,200 cy of amended soil on repository
Constructed 2,000 feet of runoff/run-on channels
Fertilized and seeded 26 acres
Planted 820 tubelings (Douglas fir, Aspen and Thimbleberry)

## Slide 48: Construction 2014

## Slide 49: UPLAND SEED MIX
Species | Common Name | Lbs PLS/acre
Upland Grasses |  | 
Elymus lanceolatus | Streambank Wheatgrass | 5.0
Pseudoroegneria spicata (ssp) | Bluebunch Wheatgrass | 5.0
Poa alpinum | Alpine Bluegrass | 7.0
Bromus marginatus | Mountain Brome | 7.0
Phleum alpinum | Alpine Timothy | 7.0
Festuca ovine | Sheep Fescue | 5.0
Forbs |  | 36.0
Aquilegia flavescens | Yellow Columbine | 0.5
Linum lewisii | Lewis Blue Flax | 0.5
Non-Native Annuals |  | 1.0
Regreen | Sterile wheat | 15
 |  | 52.0 PLS/ac

## Slide 50: RIPARIAN SEED MIX
Species | Common Name | Lbs PLS/acre
Grasses |  | 
Dechampsia caespitosa | Tufted Hairgrass | 6.0
Phleum alpinum | Alpine Timothy | 6.0
Calamagrostis canadensis | Bluejoint Reedgrass | 5.0
Poa alpina | Alpine Bluegrass | 5.0
Grass-like |  | 22.0
Carex nebrascensis | Nebraska Sedge | 1.0
Juncus articus (ssp) littoralis | Baltic Rush | 1.0
Forbs |  | 2.0
Erigeron speciosus | Aspen Daisy | 3.0
 |  | 25.0 PLS

## Slide 51: Construction 2014

## Slide 52: Construction 2014
Summer Erosion Control

## Slide 53: Construction 2014

## Slide 54: Construction 2014

## Slide 55: Construction 2014

## Slide 56: Construction 2014
September 18th

## Slide 57: Construction 2014
September 19th

## Slide 58: Final Project Quantities
Repository contains 245,000 cubic yards of compacted lime stabilized tailings and waste rock
13,512 tons of quick lime used for tailings stabilization
4,840 dry tons of compost
Soda Butte and Miller Creek - 1,797 feet
Constructed 4,000 feet of storm water channels
Re-Vegetated 26 acres
The McLaren Reclamation project was completed 1 year ahead of schedule and $2.5 million under budget

## Slide 59: Soda Butte Creek
2008 2013

## Slide 60: June 2015

## Slide 61: June 2015

## Slide 62: June 2015

## Slide 63: July 2015

## Slide 64: July 2015

## Slide 65: October 2015

## Slide 66: 2016

## Slide 67: 2016

## Slide 68: 2017

## Slide 69: 2017

## Slide 70
STAKE HOLDERS:
Montana Department of Environmental Quality/Mine Waste Cleanup Bureau
    John Koerth
    Autumn Coleman
    Tom Henderson
Cooke City Residents
Beartooth Alliance,
Gallatin National Forest, and
Yellowstone National Park
2014 American Council of Engineering Companies (ACEC) awarded the State and National Engineering Excellence Award in the Environmental category to Montana DEQ and Pioneer.

## Slide 71: Costs Funding
COSTS
Total Construction Cost $21,897,248.55
Total Engineering Costs $2,027,851.85
    FUNDING
U.S. Department of Interior Office of Surface Mining (OSM) $23,000,000
Department of Natural Resources Conservation $300,000

## Slide 72: 2015 to Present
September 2015 and 2016 FWP and NPS removed all non-native species from Soda Butte for Cutthroat
    Soda Butte Creek 303(d) Listing
    Soda Butte Creek Water Quality Study 2015
        Montana Institute of Ecosystems, MT DEQ and YNP
        Conclusion – Soda Butte Creek below the former tailings site now contributes marginally to total loads
        2018 Soda Butte Creek Removed from 303(d) List

## Slide 73: Questions