## Slide 1: PREDICTION OF OPTICAL AND NON-OPTICAL WATER QUALITY PARAMETERS IN OLIGOTROPHIC AND EUTROPHIC SYSTEMS USING A SMALL UNMANNED AERIAL SYSTEM
Juan G. Arango and Robert W. Nairn
University of Oklahoma
36th Annual Meeting of the American
Society of Mining & Reclamation
Notes: First of all, I want to thank you all for being part of my committee, as I have mentioned several times in my emails it is an honor for me to have you guys as contributing members in this project. Today I will be presenting to you my PhD research prospectus, that I have tile (READ TITLE).

## Slide 2
Introduction
Hypothesis and Objectives
Methodology
Results

## Slide 3: REMOTE SENSING
Notes: An energy source, in this case the sun emits energy. That incident energy hits a target (paved roads, bare soil, water, grass, a forest or a built-up area) and the reflected energy from each target gets sense and recorded by a sensor onboard a satellite.

## Slide 4: ENERGY INTERACTIONS WITH TARGETS
Notes: An energy source, in this case the sun emits energy. That incident energy hits a target (paved roads, bare soil, water, grass, a forest or a built-up area) and the reflected energy from each target gets sense and recorded by a sensor onboard a satellite.

## Slide 5: SPECTRAL SIGNATURES
Notes: An energy source, in this case the sun emits energy. That incident energy hits a target (paved roads, bare soil, water, grass, a forest or a built-up area) and the reflected energy from each target gets sense and recorded by a sensor onboard a satellite.

## Slide 6: EARTH OBSERVATION SATELLITES
Satellite | Launched Year | Spatial Resolution | Temporal Resolution (Day) | Spectral Resolution | Radiometric Resolution
Landsat-5 | 1984 | 30 m. multispectral 120 m. TIR | 16 | Blue, Green, Red, NIR, SWIR-1, SWIR-2, TIR | 8-bit
OrbView–2 | 1997 | 1130 m. | 1 | 8 bands (0.402 to 0.885 μm) | 12-bit
IKONOS | 1999 | 1 m. panchromatic 4 m. multispectral | 3 | Panchromatic, Blue, Green, Red, NIR | 11-bit
Landsat-7 | 1999 | 15 m. panchromatic 30 m. multispectral 60 m. TIR | 16 | Panchromatic, Blue, Green, Red, NIR, SWIR-1, SWIR-2, TIR | 12-bit
Terra - MODIS | 1999 | 250 m. B1 – B2 500 m. B3 – B7 1000 m. B8 – B36 | 1-2 | 36 bands (0.620 – 14.385 μm) | 12-bit
EO-1 ALI | 2001 | 10 m. panchromatic 30 m. multispectral | 16 | 10 bands (0.450 – 2.350 μm) | 12-bit
QuickBird-2 | 2001 | 3 m. panchromatic 15 m. multispectral | 1-3 | Panchromatic, Blue, Green, Red, NIR | 8-bit
OrbView-3 | 2003 | 1 m. panchromatic 4 m. multispectral | 3 | Panchromatic, Blue, Green, Red, NIR | 11-bit
GeoEye-1 | 2008 | 0.41 m. panchromatic 1.64 m. multispectral | 3 | Panchromatic, Blue, Green, Red, NIR | 11-bit
Landsat-8 | 2013 | 15 m. panchromatic 30 m. multispectral 60 m. TIR | 16 | Panchromatic, Coastal, Blue, Green, Red, NIR, SWIR-2, SWIR-4, TIR | 12-bit
Gaofen-1 | 2013 | 2.0 m. panchromatic 8 m. multispectral | 4 | Panchromatic, Blue, Green, Red, NIR | 14 -bit
Sentinel-2 | 2015 | 10 m. multispectral 20 m. 60 m. | 5 | 13 bands (0.43 – 2.28 μm) | 12-bit
GeoEye-2 | 2016 | 0.31 m. panchromatic 1.24 m. multispectral | 3 days | Panchromatic, Blue, Green, Red, NIR | 11-bit
Notes: An energy source, in this case the sun emits energy. That incident energy hits a target (paved roads, bare soil, water, grass, a forest or a built-up area) and the reflected energy from each target gets sense and recorded by a sensor onboard a satellite.

## Slide 7: EOS – MINING WATER BODIES
Mayer Ranch - True Color Image 04/23/2013 – Quickbird
Collapse Feature - True Color Image 09/27/2011 – Landsat
Notes: An energy source, in this case the sun emits energy. That incident energy hits a target (paved roads, bare soil, water, grass, a forest or a built-up area) and the reflected energy from each target gets sense and recorded by a sensor onboard a satellite.

## Slide 8: EOS – MINING WATER BODIES
Tailings Pond - True Color Image 09/27/2011 – Landsat
Collapse Feature - True Color Image 06/15/2009 – Quickbird
Notes: An energy source, in this case the sun emits energy. That incident energy hits a target (paved roads, bare soil, water, grass, a forest or a built-up area) and the reflected energy from each target gets sense and recorded by a sensor onboard a satellite.

## Slide 9: EOS SATELLITE LIMITATIONS
Data lost due to cloud coverage
Only optical variables:
  Chl-a
  Turbidity
  SDD
  TSS
Notes: An energy source, in this case the sun emits energy. That incident energy hits a target (paved roads, bare soil, water, grass, a forest or a built-up area) and the reflected energy from each target gets sense and recorded by a sensor onboard a satellite.

## Slide 10: HYPOTHESIS AND OBJECTIVES
Notes: An energy source, in this case the sun emits energy. That incident energy hits a target (paved roads, bare soil, water, grass, a forest or a built-up area) and the reflected energy from each target gets sense and recorded by a sensor onboard a satellite.

## Slide 11: HYPOTHESIS
A combination of bands from images captured by a multispectral sensor attached to an sUAS can predict optical (TSS, Chl-a, SDD) and non-optical (TP, TN) water quality parameters in reservoirs with different trophic states
By having the ability to capture free cloud images at a finer spatial resolution, sUAS models that predict optical and non-optical water quality parameters have the ability to generate more accurate data, than the models that rely on satellite data
Notes: An energy source, in this case the sun emits energy. That incident energy hits a target (paved roads, bare soil, water, grass, a forest or a built-up area) and the reflected energy from each target gets sense and recorded by a sensor onboard a satellite.

## Slide 12: OBJECTIVES
To develop statistical models capable of predicting optical (TSS, Chl-a, SDD) and non-optical (TP, TN) water quality parameters in reservoirs with different trophic states
To statistically compare and evaluate the accuracy of the data generated by water quality models that rely on satellite imagery and sUAS imagery
Notes: An energy source, in this case the sun emits energy. That incident energy hits a target (paved roads, bare soil, water, grass, a forest or a built-up area) and the reflected energy from each target gets sense and recorded by a sensor onboard a satellite.

## Slide 13: METHODOLOGY
Notes: An energy source, in this case the sun emits energy. That incident energy hits a target (paved roads, bare soil, water, grass, a forest or a built-up area) and the reflected energy from each target gets sense and recorded by a sensor onboard a satellite.

## Slide 14: METHODOLOGY
Phase 1
Phase 2
Phase 3

## Slide 15: DATA COLLECTION AND ANALYSIS
MULTISPECTRAL DATA COLLECTION
Analyte | Method
Chlorophyll α | EPA 445.0
Total Phosphorus | EPA 365.3
Total Nitrogen | Multi N/C 2100S
Nitrate-Nitrogen | EPA 352.1
Ammonia-nitrogen | HACH 10031
Total Suspended Solids | EPA 160.2
Secchi Disk | -
LABORATORY ANALYSIS
Notes: An energy source, in this case the sun emits energy. That incident energy hits a target (paved roads, bare soil, water, grass, a forest or a built-up area) and the reflected energy from each target gets sense and recorded by a sensor onboard a satellite.

## Slide 16: SCENARIO EVALUATION

## Slide 17: MODEL DEVELOPMENT
  Model Development (50% Data)
  Regression analyses
  Water quality parameter (dependent variable)
  Refraction data from multispectral image (independent variable)
Best Fit Determination
  Coefficient of determination (R2)
  Akaike Information Criterion (AIC)
Model Validation (50% Data)
  Statistically comparison between in-situ water quality parameter measurements and predicted measurements

## Slide 18: STUDY AREA
Notes: Oligotrophic = Nursery Ponds
Eutrophic = WWL

## Slide 19: RESULTS
Notes: An energy source, in this case the sun emits energy. That incident energy hits a target (paved roads, bare soil, water, grass, a forest or a built-up area) and the reflected energy from each target gets sense and recorded by a sensor onboard a satellite.

## Slide 20: SINGLE VARIABLE RESULTS
Total of 315 (single variable) linear models
  Point Extraction = 105
  Buffer Extraction =105
  Kriging Extraction = 105
Notes: Oligotrophic = Nursery Ponds
Eutrophic = WWL

## Slide 21: MODEL DEVELOPMENT
  Model Development (50% Data)
  Regression analyses
  Water quality parameter (dependent variable)
  Refraction data from multispectral image (independent variable)
Best Fit Determination
  Coefficient of determination (R2)
  Akaike Information Criterion (AIC)
Model Validation (50% Data)
  Statistically comparison between in-situ water quality parameter measurements and predicted measurements

## Slide 22: LINEAR MODELS - EVALUATION
Notes: An energy source, in this case the sun emits energy. That incident energy hits a target (paved roads, bare soil, water, grass, a forest or a built-up area) and the reflected energy from each target gets sense and recorded by a sensor onboard a satellite.

## Slide 23: POINT EXTRACTION RESULTS
TSS = 37.317*(Green/Red) - 47.273 (R2= 0.821 p= 5.87e-7)R2R
2
SD = -786.440*(Green) + 72.929 (R2= 0.780 p= 2.56e-6)
Chl-a = 202.84*(Green/Red) - 262.58 (R2= 0.810 p= 8.52e-7)
TN = 7.0435*(Green/Red) - 8.5676 (R2= 0.844 p= 1.885e-7)
TP = 1.8392 *(Green/Red) - 2.4117 (R2= 0.831 p= 3.46e-7)
Notes: An energy source, in this case the sun emits energy. That incident energy hits a target (paved roads, bare soil, water, grass, a forest or a built-up area) and the reflected energy from each target gets sense and recorded by a sensor onboard a satellite.

## Slide 24: BUFFER EXTRACTION RESULTS
TSS = 37.361*(Green/Red) - 51.626 (R2= 0.759 p= 1.09e-5)R2R
2
SD = -875.989*(Green) + 77.687 (R2=0.605 p= 2.469 e-6)
Chl-a = 199.75*(Green/Red) - 280.56 (R2= 0.730 p= 2.47e-7)
TN = 6.991*(Green/Red) - 9.273 (R2= 0.768 p= 8.39e-6)
TP = 1.8464*(Green/Red) - 2.6307 (R2= 0.764 p= 9.56e-6)
Notes: An energy source, in this case the sun emits energy. That incident energy hits a target (paved roads, bare soil, water, grass, a forest or a built-up area) and the reflected energy from each target gets sense and recorded by a sensor onboard a satellite.

## Slide 25: ORDINARY KRIGING – NURSERY POND -A
TN
TP
Notes: An energy source, in this case the sun emits energy. That incident energy hits a target (paved roads, bare soil, water, grass, a forest or a built-up area) and the reflected energy from each target gets sense and recorded by a sensor onboard a satellite.

## Slide 26: ORDINARY KRIGING – NURSERY POND - B
TN
TP
Notes: An energy source, in this case the sun emits energy. That incident energy hits a target (paved roads, bare soil, water, grass, a forest or a built-up area) and the reflected energy from each target gets sense and recorded by a sensor onboard a satellite.

## Slide 27: ORDINARY KRIGING – WASTEWATER LAGOON
TN
TP
Notes: An energy source, in this case the sun emits energy. That incident energy hits a target (paved roads, bare soil, water, grass, a forest or a built-up area) and the reflected energy from each target gets sense and recorded by a sensor onboard a satellite.

## Slide 28: KRIGING EXTRACTION RESULTS
TSS = 31.694*(Green/Red) - 35.248 (R2= 0.787 p= 1.19e-78)R2R
2
SD = -875.989*(Green) + 77.687 (R2=0.699 p= 7.75e-58)
Chl-a = 199.75*(Green/Red) - 280.56 (R2= 0.687 p= 1.34e-59)
TN = 6.2312*(Green/Red) - 6.8654 (R2= 0.799 p= 6.39e-82)
TP = 1.71343*(Green/Red) - 2.04546 (R2= 0.798 p= 1.71e-81)
Notes: An energy source, in this case the sun emits energy. That incident energy hits a target (paved roads, bare soil, water, grass, a forest or a built-up area) and the reflected energy from each target gets sense and recorded by a sensor onboard a satellite.

## Slide 29: MODEL DEVELOPMENT
  Model Development (50% Data)
  Regression analyses
  Water quality parameter (dependent variable)
  Refraction data from multispectral image (independent variable)
Best Fit Determination
  Coefficient of determination (R2)
  Akaike Information Criterion (AIC)
Model Validation (50% Data)
  Statistically comparison between in-situ water quality parameter measurements and predicted measurements

## Slide 30: POINT EXTRACTION VALIDATION

## Slide 31: MULTIPLE VARIABLE RESULTS
Total of 15 (multiple variable) linear models
  Point Extraction
Model Evaluation
  Analysis of Variance (ANOVA)
Notes: Oligotrophic = Nursery Ponds
Eutrophic = WWL

## Slide 32: MULTIPLE VARIABLE VALIDATION

## Slide 33: SINGLE VS. MULTIPLE VARIABLE
Parameter | Single Variable Model | R2 | Multi Variable Model | R2
SD | lm(formula = SD.sub$SD ~ SD.sub$PointGreen) | 0.7809 | lm(formula = SD.Mod.Data$SD ~ SD.Mod.Data$B.R + SD.Mod.Data$G.R + SD.Mod.Data$G.B) | 0.8883
TSS | lm(formula = TSS.sub$TSS ~ TSS.sub$G.R) | 0.8211 | lm(formula = TSS.Mod.Data$TSS ~ TSS.Mod.Data$B.R + TSS.Mod.Data$G.B + TSS.Mod.Data$G.R) | 0.9869
TN | lm(formula = TN.sub$TN ~ TN.sub$G.R) | 0.8446 | lm(formula = TN.Mod.Data$TN ~ TN.Mod.Data$B.R + TN.Mod.Data$G.B + TN.Mod.Data$G.R) | 0.9793
TP | lm(formula = TP.sub$TP ~ TP.sub$G.R) | 0.8316 | lm(formula = TP.Mod.Data$TP ~ TP.Mod.Data$B.R + TP.Mod.Data$G.B + TP.Mod.Data$G.R) | 0.9835
Chl-a | lm(formula = Chloro.a.sub$Chloro.a ~ Chloro.a.sub$G.R) | 0.8104 | lm(formula = CHL.A.Mod.Data$Chloro.a ~ CHL.A.Mod.Data$PointGreen + CHL.A.Mod.Data$PointRed) | 0.846

## Slide 34: NURSERY POND – WATER QUALITY OPTICAL PARAMETERS
Secchi Disk
Total Suspended Solids
Chlorophyll – A

## Slide 35: NURSERY POND – WATER QUALITY NON- OPTICAL PARAMETERS
Total Phosphorus
Total Nitrogen

## Slide 36: WASTEWATER LAGOONS – WATER QUALITY OPTICAL PARAMETERS
Secchi Disk
Total Suspended Solids
Chlorophyll – A

## Slide 37: WASTEWATER LAGOONS – WATER QUALITY NON- OPTICAL PARAMETERS
Total Nitrogen
Total Phosphorus

## Slide 38: FINAL CONCLUSIONS
Optical and non-optical water quality parameters can be predicted using sUAS
Statistical interpolation (ordinary kriging) does not improve the relationship between the different water quality parameters and the reflectance values. More doesn’t mean better!
Single linear models have the capability to predict different water quality parameters; however, multiple linear models can explain these relationships in a better way (higher R2)

## Slide 39: ACKNOWLEDGMENTS
City of Commerce, OK
Brandon Holzbauer Schweitzer (CREW)
Maggie Tang (CREW)

## Slide 40: THANK YOU QUESTIONS?
In memory of Gonzalo E. Arango
Gracias papá! Te extraño