## Slide 1: Restoration
We create solutions that build better communities
French Gulch & Moose Creek
Notes: Quick intro and background

## Slide 2: Outline
French Gulch & Moose Creek Restoration
Project Planning
Survey and Design
Construction Process
Monitoring Post Construction
Enhancements
Future Monitoring
Take Home Lessons
Notes: Quick outline of presentation topics

## Slide 3
Others:
Montana Civil Contractors
Watershed Consulting
R & S Johnson Construction
Pioneer Technical
Montana Conservation Corps
Notes: Project owners, agency, design team, contractors

## Slide 4: Project Location
Project Location
Anaconda Smelter Impacts
Notes: Describe location, SW of Butte. Private individual mines from 1800s

## Slide 5: Project Location
Notes: Public lands, watershed restoration

## Slide 6: Project Location
Notes: Public lands, watershed restoration

## Slide 7: History of Mining
Upstream project limit
French Gulch & Moose Creek Restoration
Notes: Past impacts from dredge mining and Anaconda smelter 1913

## Slide 8
Notes: Past impacts from dredge mining and Anaconda smelter 1913

## Slide 9
Notes: Past impacts from dredge mining and Anaconda smelter 1913

## Slide 10: In 2016
Old French Creek
New Hwy 569
Dredge Mine Piles
New French Creek
Notes: Pre-project site and other work on HWY

## Slide 11: Field Investigations
Notes: Field work to survey topo, characterize impacts, find functioning sections.

## Slide 12: Project Objectives
Restore spawning habitat for native trout species.
Increase sediment retention.
Reduce conifer encroachment on riparian areas.
Remove mine dredge piles to restore stream/floodplain.
Remove fish passage barrier.
Relocate existing road from floodplain.
Notes: Project objectives to restore stream and fish habitat, restore sediment retention

## Slide 13: Prioritized Restoration
Geomorphic Comparison |  |  |  | 
 | Impact | Reference |  | Difference
Bankfull Width: | 7.9 | 5.9 | ft | 32%
Floodprone Width: | 22 | 53 | ft | 59%
% Pools: | 12.0 | 50.5 | % | 76%
Meander Length: | 224 | 49 | ft | 356%
Notes: Quantify impacts and degree of need

## Slide 14: Prioritized Restoration
French Gulch & Moose Creek Restoration
Notes: Design segments of re-construction

## Slide 15: Project Funding
Notes: Many agency and NGOs part of funding project

## Slide 16: Hwy 569
Notes: Highway reconstruction required coordination

## Slide 17: Hwy 569
Notes: Highway reconstruction required coordination

## Slide 18: Design
Design
Notes: Detailed analysis for final design

## Slide 19: Design
French Gulch & Moose Creek Restoration
Notes: Detailed analysis for final design

## Slide 20: Design
Notes: Multiple restoration approaches in one project, value engineering

## Slide 21: Design
French Gulch & Moose Creek Restoration
Notes: Multiple restoration approaches in one project, value engineering

## Slide 22
Notes: Multiple restoration approaches in one project, value engineering

## Slide 23: Construction
Notes: Dirt work and salvage efforts

## Slide 24: Construction
French Gulch & Moose Creek Restoration
Notes: Dirt work and salvage efforts

## Slide 25: Construction
Notes: Dirt work and salvage efforts

## Slide 26
Notes: Design flexibility to suit site conditions, construction survey

## Slide 27
Notes: Design flexibility to suit site conditions, construction survey

## Slide 28: Construction
French Gulch & Moose Creek Restoration
Notes: Design flexibility to suit site conditions, construction survey

## Slide 29
Notes: Design flexibility to suit site conditions, construction survey

## Slide 30: Construction
French Gulch & Moose Creek Restoration
Notes: Moose Creek, floodplain re-connection

## Slide 31: Construction
French Gulch & Moose Creek Restoration
Notes: Additional dredge impact removals, FP roughness with onsite materials

## Slide 32: Construction
8 acres new floodplain/wetlands
30,000+ cubic yards of mine tailings removed from floodplain
7,400 feet new stream channel with complex habitat
1 fish passage barrier removed
2,200+ riparian container plants
Notes: Recap of 2016 field season

## Slide 33: Monitoring
Notes: 2017 re-survey and monitoring of stream reach

## Slide 34: Monitoring
Notes: 2017 re-survey and monitoring of stream reach

## Slide 35
Notes: Sediment load TMDL allocations, monitoring data by reach

## Slide 36
Notes: Sediment load TMDL allocations, monitoring data by reach

## Slide 37: 2017 Enhancements
Notes: Remaining funds to construction off-stream floodplain, riparian and wetlands expansions

## Slide 38: 2017 Enhancements
Notes: Remaining funds to construction off-stream floodplain, riparian and wetlands expansions

## Slide 39
Notes: 2018 site photos

## Slide 40: Moving Forward
Notes: Thoughts and lessons

## Slide 41: Moving Forward
Notes: Thoughts and lessons

## Slide 42: Lower French Creek
Notes: Current project, improved information use, address fine sediment delivery

## Slide 43
Notes: Current project, improved information use, address fine sediment delivery

## Slide 44: Lower French Creek
Notes: Current project, improved information use, address fine sediment delivery

## Slide 45: Lower French Creek
Notes: Improved clarity

## Slide 47: Lower French Creek
Notes: Improved clarity

## Slide 48: Questions?
Matt Barnes, PE, CFM
406-495-3482 | mbarnes@m-m.net
Notes: Thank you!