## Slide 1: Abandoned Mine Lands: Cleanup Challenges and Technology Opportunities
American Society of Mining and Reclamation
June 4, 2019

## Slide 2: The Site Universe
No comprehensive national inventory of abandoned mine lands (AML) in the U.S., estimates range from 100,000 to 500,000 sites
Superfund Enterprise Management System (SEMS) contains less than 0.1 percent of this large AML universe
There are more than 50,000 abandoned coal mines, which fall under the jurisdiction of the Office of Surface Mining Reclamation and Enforcement as well as authorized states

## Slide 3: Superfund Mine / Mineral Processing Sites
140 Superfund sites (Superfund National Priorities List [NPL] or Superfund Alternative Approach) are mining and mineral processing sites:
  More than half are greater than 500 acres in size; Bunker Hill Mining and Metallurgical Complex site (a.k.a., Coeur d’Alene Basin; Idaho and Washington), which covers 1,500 sq miles, is largest
  Mine-influenced waters will need to be addressed at more than 30 percent of these sites
  EPA Superfund program has estimated expenditures of more than $4B to address mining and mineral processing sites to date (does not capture all costs PRPs have spent to date)

## Slide 4: National Priorities List Mining Sites Remedy Components

## Slide 5: A Continued Need for Innovation
Drivers include:
  Mining site universe: large number of sites, common problems
  Timelines and long-term costs
  Interest in innovation: “demand pull”
    Public and private problem-holders
    Leadership attention
    Communities, economic development
    Big problem/larger window of opportunity
  Research programs/results: “supply push” (?)

## Slide 6: Target Areas of Innovation
Treatment of mine-influenced waters (MIW)
Source treatment/tailings/waste rock/underground workings
Site revitalization and reuse
Mineral resource recovery
Characterization and monitoring tools
Involve
  Chemistry, biology
  Geology, hydrogeology
  Engineering

## Slide 7: Key Considerations for Innovation
Legal issues
  Liability
  Complex ownership (Mixed Ownership)
  Intellectual property
Funding and human resources
Health and safety
Transferring experience, lessons
  Documenting results
  Quality assurance

## Slide 8: Key Considerations for Innovation
Scalability: from the bench to field to full-scale use
  Harsh, cold realities
  Time: not always a short process
  Site differences
  Documentation, communication, and “urban legend”
Project level: present-oriented, technologies ready now
Available site information, characterization
Researcher to entrepreneur
Inertia: “this is the way we’ve always done it”

## Slide 9: Technology Development
This Photo by Unknown Author is licensed under CC BY-SA
Idea/Proof of Concept
Bench scale testing
Pilot scale technology
Full scale technology
Commercial availability
Acceptance
Field testing
Scaling
Investment/funding
Information transfer
Familiarity/early adopters
Procurement

## Slide 10: Collaboration is Essential
Many information needs
  Many decisions/decisionmakers
  Many perspectives
Research is spread out
  Agencies/Federal funding
  Private sector research
  Funding, technology incubation
Leveraging vs. duplicating

## Slide 11: Technology Acceptance: Multiple Decisionmakers, Diverse Decision Needs
Responsible Party/Owner Operator
State/Federal Project Manager
Consulting Engineer
Technology Vendors, Researchers, Investors
Local officials
Developers
Lenders
Community

## Slide 12: Innovation is Not a Linear Process
Full-scale field use
Field testing/ demo
Pilot testing
Bench scale develop-ment
Basic Research
Feedback: experience, issues, needs
Response: modify, optimize, new solutions
This Photo by Unknown Author is licensed under CC BY-NC-ND

## Slide 13: Innovation Happens
Innovation is happening
  Case examples
  Research and development
  But…
It’s a tough crowd: “If there were other options, we’d use them” or “Nothing else is ready to go now.”
Innovation requires patience
Innovation is both technology and approach based
No single path to acceptance; process is adaptive

## Slide 14: Existing Avenues of Innovation
Biological/Biochemical Treatment
Ecological restoration
Passive and semi-passive treatment
Engineering controls
Greener remediation
Site characterization, data use/management
Upcoming (2020) mining technology update, Handbook of Capabilities of Remedial Technologies for Use at Mining Waste Sites

## Slide 15: Technologies
Anoxic limestone drains
Successive alkalinity producing systems
Aluminator
Constructed wetlands
Biochemical reactors

## Slide 16: Technologies
Phytotechnologies ( http://cluin.org/products/phyto/ )
Permeable reactive barriers
Fluidized bed reactors
Reverse osmosis
Zero valent iron

## Slide 17: Technologies
Rotating cylinder treatment systems
Ferrihydrite adsorption
Electrocoagulation
Ion exchange
Biological reduction
Ceramic microfiltration

## Slide 18: Selection of P&T Continues to Decline and Selection of In Situ Treatment Is Steady (FY 1985-2017)
Chart: Percentage of Groundwater Decision Documents
| 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
P&T | 0.79412 | 0.69355 | 0.77083 | 0.82796 | 0.78824 | 0.80702 | 0.85075 | 0.7732 | 0.71028 | 0.71845 | 0.59615 | 0.58763 | 0.4375 | 0.37778 | 0.5 | 0.49451 | 0.43836 | 0.52542 | 0.33333 | 0.35385 | 0.41026 | 0.23711 | 0.28866 | 0.32308 | 0.25676 | 0.17333 | 0.22951 | 0.25862 | 0.26 | 0.16667 | 0.21429 | 0.2 | 0.18182
In Situ Treatment | 0.029412 | 0.032258 | 0.041667 | 0.021505 | 0.12941 | 0.078947 | 0.10448 | 0.12371 | 0.084112 | 0.1165 | 0.14423 | 0.12371 | 0.16071 | 0.21111 | 0.175 | 0.23077 | 0.26027 | 0.28814 | 0.28205 | 0.27692 | 0.26923 | 0.34021 | 0.30928 | 0.32308 | 0.39189 | 0.38667 | 0.37705 | 0.41379 | 0.58 | 0.55556 | 0.5 | 0.48571 | 0.54545

## Slide 19: Recently Selected Groundwater Remedies (FY 2015–17) Groundwater Decision Documents = 111
Remedy | Total (FY15-17) | Percent Groundwater Decision Documents
Ex Situ Treatment (P&T) | 22 | 20%
In Situ Treatment | 57 | 51%
Bioremediation | 30 | 27%
Bioremediation (anaerobic, insitu) | 20 | 18%
Bioremediation (bioaugmentation, insitu) | 11 | 10%
Bioremediation (aerobic, insitu) | 5 | 5%
Bioremediation (other, NOS, insitu) | 4 | 4%
Chemical Treatment | 26 | 24%
Chemical Oxidation (insitu) | 19 | 17%
Chemical Reduction (insitu) | 8 | 7%
Neutralization (insitu) | 1 | 1%
Thermal treatment | 6 | 5%
Permeable Reactive Barrier | 6 | 5%
Multi-phase Extraction | 4 | 4%
Air Sparging | 3 | 3%
Unspecified in situ treatment | 3 | 3%
Vapor Extraction | 3 | 3%
Electrokinetics | 1 | 1%
Flushing | 1 | 1%
Phytoremediation | 1 | 1%
Solidification/Stabilization | 2 | 2%

## Slide 20: P&T Remedies Almost Always Combined with Other Remedies, Especially Source Control (FY 1982-2017)
MNA = monitored natural attenuation
P&T = pump and treat (selected at 834 sites)
Chart: 
| P&T, Source Treatment and On-site Containment or Off-site Disposal | P&T and Source Treatment | P&T and Source On-site Containment or Off-site Disposal | P&T and In Situ Treatment for Groundwater | P&T and MNA for Groundwater | P&T, In Situ Treatment and MNA for Groundwater | P&T only for Groundwater
 | 514 | 81 | 131 | 20 | 17 | 6 | 76

## Slide 21: We can leverage existing infrastructure, opportunities
EPA Waste Programs and Technology Innovation, 25+ years of experience
  Information exchange
  Training
  Communication, distance learning
  Research capabilities and demonstration experience
Other Federal programs, academic, private sector
  Owners
  Research
Collaboration and relationships/existing work groups, associations, etc.

## Slide 22: Examples of Resources
Hazardous Waste Cleanup Information (CLUIN) Web Site
Information
Online Training
https://cluin.org
Best Practice Guides and Case Studies
Training
CERCLA Education Center
ERT Training Program
https://trainex.org
Interstate Technology Regulatory Council (ITRC)
Technical Guidance
Training
https://www.itrcweb.org
ETV and ISO Standards, Guidance
Federal Research, e.g., Superfund Research Program-National Institute of Environmental Health Sciences (NIEHS)
www.niehs.nih.gov
Federal Collaboration (e.g., FRTR and FMD)
EPA Office of Research and Development

## Slide 23: Charting a Course to Innovation
Demonstrating/evaluating technologies
  Technology identification: intersection of priorities and technologies ready for evaluation at field level
  Site identification
  Evaluation framework: based on existing ISO ETV, EPA ETV and SITE procedures, tools
Increasing acceptance by supporting decisionmakers
  Build collaboration among decisionmakers/leverage work
  Information dissemination and educational resources
  Leadership commitment/encouragement

## Slide 24: Charting a Course to Innovation
Individual demonstrations will not lead to technology use, acceptance. Requires sharing and building on information, use at multiple sites. Not solely a function of formal demonstration or verification programs
Technology demonstration has multiple levels
  Field access to support research
  Field demonstration to support transition to field-scale, commercial scale technology availability
  Pilot or treatability testing to support selection at sites, raise comfort of regulators, site owners, and contractors

## Slide 25: Charting a Course to Innovation
Information exists, projects underway. Need to build comprehensive understanding, access to information
Link between technical support and research is essential
We can’t do it alone
Where do we go from here?

## Slide 26: Contact Information
Shahid Mahmud, Team Leader, EPA National Mining Team
Office of Superfund Remediation and Technology Innovations
U.S. Environmental Protection Agency
Phone: 703-603-8789
Email: mahmud.shahid@epa.gov
Michele Mahoney, Team Leader, Mining Technologies
Office of Superfund Remediation and Technology Innovations
U.S. Environmental Protection Agency
Phone: 703-603-9057
Email: mahoney.michele@epa.gov
Ed Gilbert, Chief, Technology Assessment Branch
Office of Superfund Remediation and Technology Innovations
U.S. Environmental Protection Agency
Phone: 703-603-8883
Email: gilbert.edward@epa.gov
Daniel Powell, Chief, Technology Integration and Information Branch
Office of Superfund Remediation and Technology Innovations
U.S. Environmental Protection Agency
Phone: 703-603-7196
Email: powell.dan@epa.gov