## Slide 1: Ecological Restoration Planning for Coal Mining Areas in China and Case Studies
Zhenqi Hu1,2 胡振琪1,2
Wu Xiao1,2 肖武1,2
1.Institute of Land Reclamation & Ecological Restoration
China University of Mining and Technology(Beijing)
1.中国矿业大学（北京），土地复垦与生态重建研究所
2. Engineering Research Center of Mining Environment & Ecological Safety, Ministry of Education
2.矿山生态安全教育部工程研究中心
中国煤矿区生态修复规划及其案例

## Slide 2: Outline
1. Introduction
引言
2. Ecological Restoration Planning for Abandoned Coal Mines
废弃矿区的生态修复规划
3. Ecological Restoration Planning for Active Coal Mines
正在开采矿区的生态修复规划

## Slide 3: 1. Introduction 引言
Coal resources distribution in China
中国煤炭资源分布图
Coal is China’s most abundant, important, and widely distributed fossil fuel resource.
煤炭是中国最丰富、最重要，也是应用最广泛的化石能源。

## Slide 4
China’s coal production was 3.8 billion tons in 2014. 90% from underground mining
2014年中国煤炭产量达到38亿吨，而90%的煤矿为井工矿
Coal yield and growth rate from 1990 to 2010 in China
1990-2010中国煤炭产量与增长率
1. Introduction 引言

## Slide 5: Impact of coal mining on environment in China
Coal mining has produced a lot of environmental problems while it makes great contribution to economic growth

## Slide 6
给
Southern南部地区：
mining subsidence induced landslide and mudslides, 开采沉陷引发的滑坡和泥石流
groundwater loses 地下水流失
Eastern东部地区：
Mining subsidence induced ponds area, 下沉积水
farmland lose, 耕地减少
Village movements 村庄搬迁
东
补
带
带
部
中
供
自
Northwest 西北地区：
Mining subsidence induced cracks and fissures;
开采沉陷引发的地表裂缝和裂纹；
Soil erosion; 水土流失；
Acid coal waste dumps spontaneous combustion;
酸性煤矸石山的自燃
Land occupation by surface mining露天开采的土地压占
Impacts of coal mining on eco-environment vary in different part of China

## Slide 7
Land Reclamation and ecological restoration
has become an urgent task in China
In General,
Restoration planning is very important for repairing the environment in mining areas.
it is a basis of restoration engineering.
it is a basis of regional environmental protection , economic development and ecological civilization construction.

## Slide 8
给
东
补
带
带
部
中
供
自
Case studies
Liaoyuan National Mining Museum
辽源国家矿山公园
Huainan Datong Wetland Park
淮南大通湿地公园
Hegang Subsidence land Reclamation Plan
鹤岗采煤塌陷地治理规划
Heze Subsidence land Reclamation Plan
菏泽采煤塌陷地治理规划

## Slide 9
2. Ecological Restoration Planning for Abandoned Coal Mine 废弃矿区的生态修复规划
The study area is located in Huainan City, Anhui Province
研究区位于安徽省淮南市
Huainan city
淮南
The mining history of Datong coal mine was 67 years, from 1911 to 1978, with 27.465 million tons of coals produced in total. According to surveys and estimates, the subsidence area is 2.89 km2, with a maximum subsidence of over 10 m.
淮南大通煤矿自1911年到1978年，有67年的开采历史，共开采3.7465亿吨煤炭。引发的沉陷土地约2.89km2，最大下沉深度达到10m。
Case Study No.1 – Huainan 案例一： 淮南

## Slide 10
The study area is 438 ha. The location of the study area is the transition section between the main city in the north and the new district in south and is the link between these two districts.
研究区面积438公顷，地处山北主城区和山南新区的过渡地段，是两城区之间相互联系的纽带，同时也是未来淮南城市生态环境的标志性区域之一。
Case Study No.1 – Huainan 案例一： 淮南

## Slide 11
Current situation 现状
Mining subsidence
地表沉陷
Coal waste dumps, 5 dumps
煤矸石山
3 waste yard; Garbage and water pollution
垃圾压占和水污染
Case Study No.1 – Huainan 案例一： 淮南

## Slide 12
Technical roadmap 技术路线图
Investigation and Monitoring
调查与监测
Assessment 评价
Function division and Restoration Plan
功能分区域修复 规划
Soil remediation
土壤修复
Hydrological system restoration
水系修复
Revegetation
植被恢复
Topography 地形
Remote sensing
遥感
Field investigation
实地调查
GIS
Soil contamination
土壤污染
Hydrological system水系
Biodiversity 生物多样性
Land use 土地利用
Case Study No.1 – Huainan 案例一： 淮南

## Slide 13
Function division
功能分区
Case Study No.1 – Huainan 案例一： 淮南

## Slide 14
Land use planning
Landuse Planning
土地利用规划
Case Study No.1 – Huainan 案例一： 淮南

## Slide 15
Some Restoration Treatments
修复措施
Case Study No.1 – Huainan 案例一： 淮南

## Slide 16
Results of the AML reclamation project I
修复后的大通湿地生态区
Case Study No.1 – Huainan 案例一： 淮南

## Slide 17
Wetland Restoration
湿地修复
Industrial Square Restoration
工业广场修复
Shaft Restoration
原井口修复
Wetland Restoration
湿地修复

## Slide 18
Only the region features can lead the plan of Liaoyuan National Mining Park to Success.
要占据国家矿山公园建设和发展的“一席之地”，只有突显地域特色。
Liaoyuan National Mining Park
辽源国家矿山公园
  Mining Park Distribution in China
Case Study No.2 – Liaoyuan 案例二： 辽源
The essence of Mining Park: restoration of mining area with the goal of park construction
矿山公园的实质——是以公园建设为目标的矿区生态修复

## Slide 19
  Investigation 调研
Case Study No.2 – Liaoyuan 案例二： 辽源

## Slide 20
  Data Analysis 数据分析
Case Study No.2 – Liaoyuan
Case Study No.2 – Liaoyuan 案例二： 辽源

## Slide 21
A Corridor 一廊：
About the Modern Mining History
中国近代矿业发展的历史回廊
Three Districts 三区：
Landscape districts which form the eco-isolation area.
景观集中区，形成绿色生态隔离带和生态保护屏障
Two Cores 两核：
Mining produce exhibition and experience zone
矿业生产展示、拓展体验核心区
Xi’an
西安
Shengli
胜利
Taixin泰信
Mining Relic Protection and Ecological Restoration Demonstration
矿业遗迹保护生态治理示范
Amusement and Shopping
大众休闲娱乐
观赏游乐购物
Patriotism Education and Mining History
爱国主义教育矿业情感诠释
  Function Division 功能分区
Case Study No.2 – Liaoyuan 案例二： 辽源

## Slide 22
  Special Plan - Mining Relic 专项规划—重要矿业遗迹保护规划
Case Study No.2 – Liaoyuan 案例二： 辽源

## Slide 23
  Special Plan – Natural Landscape 专项规划--典型自然景观规划
Case Study No.2 – Liaoyuan 案例二： 辽源

## Slide 24
  3、典型人文景观规划
Case Study No.2 – Liaoyuan 案例二： 辽源
  Special Plan – Cultural Landscape 专项规划--典型人文景观规划
Folk Music
二人转
Chinese Lute
“琵琶”文化
Deer
“梅花鹿”文化
Folk Painting
“农民画”文化
Miner
矿工文化

## Slide 25
Case Study No.2 – Liaoyuan 案例二： 辽源
  Aerial View of Design Sketch-鸟瞰效果图

## Slide 26
Case Study No.2 – Liaoyuan 案例二： 辽源

## Slide 27
3. Ecological Restoration Planning for Active Coal Mine
在开采矿区的生态修复规划
Ecological Restoration Planning for Active Coal Mine with Long Mining History
Case Study No.3 – Hegang 案例三：鹤岗
Built because of coal mining, Hegang is a city with long mining history, the annual output achieve 18.47 million tons.
鹤岗是一座“因煤而兴，缘煤而建”的城市，煤炭开采历史悠久，年产量将达到1847万吨/年。
Large areas of land subsidence , especially the subsidence in the urban area became an obstacle for the sustainable development.
大面积的土地塌陷，特别是很多沉陷区位于主城区内，严重影响了鹤岗的可持续发展。
Hegang city
鹤岗

## Slide 28
Impact of Subsidence to the Existing Plan
采煤沉陷地对现有规划的影响及建议
Restoration Plan for Subsidence areas
采煤沉陷地治理规划
Natural, Economic Condition
自然经济资源状况
Current Subsidence Situation
采煤沉陷地现状
Land subsidence prediction
采煤塌陷地预测
Data Collection 资料收集
Technical roadmap 技术路线图
Plan for Industrial Park
工业园区规划
Overall Urban Plan and Overall Landuse Plan
城市总体规划及土地利用总体规划
Shantytowns Reconstruction Plan
棚户区改造规划
Transportation Plan
交通线路规划
Function Division
规划功能分区
Restoration Projects
治理项目

## Slide 29
据统计，截止到2013年，鹤岗市境内采煤沉陷地共7932.12 hm2。
Case Study No.3 – Hegang 案例三：鹤岗
Current Subsidence situation
沉陷现状
According to the statistics, the total area of subsidence land was 7932.12 hm2 in 2013。

## Slide 30
9400.31hm2
2020
Mine Closure
闭矿
11993.25hm2
Case Study No.3 – Hegang 案例三：鹤岗
Subsidence Prediction
沉陷预测
Probability Integral Method

## Slide 31
2014-2020
10.8m
7.4m
7.1m
6.7m
2014-Mine Closure
21.9m
39.4m
32.9m
19.0m
Maximum Depth
Case Study No.3 – Hegang 案例三：鹤岗
Subsidence Prediction
沉陷预测

## Slide 32
2014-2020
Damage Degree Analysis
损毁程度分析
Seriously Damaged Vegetation severely impacted, cultivation and buildings destroyed.
重度损毁 地表沉陷严重，植被生长受到严重影响，农作物绝产，建筑物不能正常使用。
Medium Damaged Vegetation impacted, crop output decreases, buildings need maintenance.
中度损毁地表沉陷较严重，植被生长受到一定影响，农作物减产，建筑物需适当维修。
Slight Damaged No impact on vegetation, buildings could continue to be used.
轻度损毁地表出现轻微的变形，基本不影响植被生长，建筑物可正常使用。
Case Study No.3 – Hegang 案例三：鹤岗
Subsidence Prediction
沉陷预测

## Slide 33
优先永久治理区
Permanent Reclamation Areas
优先临时治理区
Temporary Reclamation Areas
动态治理
Dynamic Reclamation Areas
未来治理区
Future Reclamation Areas
Case Study No.3 – Hegang 案例三：鹤岗
Function Division
治理分区

## Slide 34
31 reclamation projects of 3 category has been planned during 2014 to 2020.
结合以上治理分区，本规划在近期（2014-2020年）共安排了3类31个治理重点项目。
5 Alternative Industry Projects
替代产业用地治理项目（5个）
23 Dynamic Cultivated land Reclamation Projects
动态农业用地治理项目（23个）
3 Temp Construction land Reclamation Projects
短期建设用地治理项目（3个）
Case Study No.3 – Hegang 案例三：鹤岗
Reclamation Projects
治理项目

## Slide 35
Juye Mining area located in the southwest part of Shandong Province, with 80km from south to the north, and 12km from east to the west, the coal bearing area is about 729km2
巨野矿区位于山东省西南部，南北长80km，东西宽12km，含煤面积约729㎞2。
Case Study No.4 – Heze 案例四：菏泽
巨野
矿区
Study Area
研究区概况

## Slide 36
Juye Mining area including 6 coal mines, till 2010, 4 of them started mining.
矿区由6对矿井组成，截止2010年底，已有4对投产。
Case Study No.4 – Heze 案例四：菏泽
Study Area
研究区概况

## Slide 37
Stage 1
近期(2013-2020)
Stage 2
中期(2021-2030)
Stage 3
远期(2031-2050)
Closure
闭矿(2051-2080)
The subsidence area is 63782hm2 , account 87% of the coal mine boundary, and the water logging area is 39581hm2, account for 62.1%.
塌陷面积为63782hm2，占矿区面积的87%，积水面积39581hm2，占塌陷面积的62.1%。
Case Study No.4 – Heze 案例四：菏泽
Subsidence Prediction
采煤沉陷预测

## Slide 38
Tourism District of Water Margin
水浒文化旅游区
Sightseeing High Efficiency Agriculture
观光高效农业区
Eco-economic District
水域生态经济区
Agriculture and fishery District
绿色农渔示范区
Juyun Mining Ecology Economic Belt
巨郓矿业生态经济带
East Chemical Industry Corridor
巨东化工长廊
With the goal of joint development of coal mining and agriculture, economy and ecology, based on the mining development, with consideration of local feature, to restore the land subsidence area and create an area combined with agriculture, ecology and sightseeing.
以“煤粮兼得”、经济发展和生态优化为治理目标，依托矿业发展，结合当地文化特色，通过塌陷地治理打造菏泽东部一条集农业、生态、观光等为一体的生态经济廊道。
1 Belt, 1 Corridor, 4 Districts
“一带，一廊，四区”
Case Study No.4 – Heze 案例四：菏泽
Plan Concept and Function Division
规划理念与功能分区

## Slide 39
With consideration of the subsidence rate, reclamation ability and technology, divide three stages and set the goals for each stage.
Planning Map 治理规划图
Case Study No.4 – Heze 案例四：菏泽
Reclamation Goal and Projects
治理目标与治理工程
综合考虑了巨野矿区采煤塌陷速度、治理能力、技术手段等，编制了巨野矿区的采煤塌陷地近期、中期和远期三期的治理规划、确定了各期的治理目标。

## Slide 40
Restoration Goal for each stage
各期治理目标
Case Study No.4 – Heze 案例四：菏泽
Reclamation Goal and Projects
治理目标与治理工程
Subsidence area in this stage
本期塌陷面积
Subsidence area without restoration in last stage
上期未治理面积
Restored subsidence area
治理水域面积
Subsidence area reclaimed into farmland
恢复土地面积

## Slide 41
各阶段治理布局图
First Stage
Second Stage
Last Stage

## Slide 42
Case Study No.4 – Heze 案例四：菏泽
Subsidence area after restoration
治理目标与治理工程

## Slide 43
Other Cases：Tangshan South Lake Park 其他案例：唐山南湖公园

## Slide 44
Other Cases: Huaibei National Mining Park 其他案例：淮北国家矿山公园

## Slide 45
Lake sediments reclaim district
湖泥充填复垦区
Ecological restoration district
生态修复区
Yellow river sediments reclaim district
黄河泥沙充填复垦区
Jining City locates in Shandong province, close to Yellow river.
济宁位于山东省，黄河沿岸。
It is the one of biggest coal-bases in China, Yanzhou coal company is in this city.
中国最大的产煤基地之一，兖矿集团所在地。
Subsided land : 沉陷地面积24575.79hm2 ( 2009)
Predict: 预测塌陷面积
2015: 47199.34 hm2
2020: 68100.53 hm2
Other Cases: Subsidence land Restoration Plan in Jining
其他案例：济宁市采煤塌陷地治理

## Slide 46
Other Cases: Subsidence land Restoration in Jining
其他案例：济宁市采煤塌陷地治理

## Slide 47
Thank you!!
Welcome to Institute of Land Reclamation & Ecological Restoration, China University of Mining and Technology (Beijing), and Engineering Research Center of Mining Environment & Ecological Safety, Ministry of Education