## Slide 1: Modeling the Effects of Mass Transfer in Limestone-Based Passive Treatment Systems
Joel Bandstra1, CJ Spellman2, and
Dr. William H. J. Strosnider, Ecological Engineer3
1Environmental Engineering, Saint Francis University
2Civil & Env. Engineering, University of Rhode Island
3Baruch Marine Field Lab, Univ. South Carolina

## Slide 2
Outline
Background on mass transfer in calcite dissolution kinetics
Data from an open limestone channel (OLC)
Modeling an OLC assuming MT limited kinetics
Speculation about channel geometry in OLC performance
Points of application

## Slide 3
Limestone dissolution requires mass transfer
butane.chem.uiuc.edu/pshapley/
H+
CaCO3
Ca2+
Ca2+

## Slide 4
Limestone dissolution requires mass transfer
butane.chem.uiuc.edu/pshapley/
CaCO3
Ca2+
Ca2+
[Ca]
z

## Slide 5
CaCO3
Ca2+
Ca2+
[Ca]
z
Mass transfer can limit kinetics

## Slide 6
Calcite dissolution kinetics can be MT limited
Brantley et al. Kinetics of Water-Rock Interaction (2008)

## Slide 7
Recent work suggests broader range of pH
Brantley et al. Kinetics of Water-Rock Interaction (2008)

## Slide 8
Calcite dissolution kinetics can be MT limited
Brantley et al. Kinetics of Water-Rock Interaction (2008)

## Slide 9
Outline
Background on mass transfer in calcite dissolution kinetics
Data from an open limestone channel (OLC)
Modeling an OLC assuming MT limited kinetics
Speculation about channel geometry in OLC performance
Points of application

## Slide 10
Swank Open Limestone Channel
Length 275 m
Width 1.5 m
Slope 6-9%
Avg. Flow 35 L/s
Avg. Influent
pH 3.5
Al 7.4 mg/L
Fe 0.5 mg/L
Mn 0.7 mg/L
Sampled over 4 year period for metals, pH, T, flow (at top and bottom)
Five sampling points along length of channel
Performed tracer tests

## Slide 11
Time series suggest residence time is important

## Slide 12
Residence time follows a power law w/ Q
Length 275 m
Width 1.5 m
Avg. Flow 35 L/s
Avg. Influent
pH 3.5
Al 7.4 mg/L
Fe 0.5 mg/L
Mn 0.7 mg/L

## Slide 13
Al is removed at a “low” pH
Solubility of Al:
870 mg/L

## Slide 14
High pH zone may exist near surface or in pores

## Slide 15
Outline
Background on mass transfer in calcite dissolution kinetics
Data from an open limestone channel (OLC)
Modeling an OLC assuming MT limited kinetics
Speculation about channel geometry in OLC performance
Points of application

## Slide 16
A mass transfer limited model
Implemented in PHREEQC
Inputs:
Flow & influent chemistry
…
5 m
275 m
Q, Al, Ca, pH
CaCO3
CaCO3
CaCO3
CaCO3
a
a
a
a
Ca2+ CO3-
=
Ca2+ CO3-
=
Ca2+ CO3-
=
Ca2+ CO3-
=
=
CO2
=
CO2
=
CO2
Fitting parameter:
a
Mobile
Immobile

## Slide 17
General behavior of the model
Notes: Step through the results:
-Ca goes up driven by alpha and vel.
-pH goes up, leveling out at equil
-Al is removed, first at slow rate, then at fast rate
-can be understood in terms of pH and SI

## Slide 18
Ca increases with time constant a/v
Notes: Step through the results:
-Ca goes up driven by alpha and vel.
-pH goes up, leveling out at equil
-Al is removed, first at slow rate, then at fast rate
-can be understood in terms of pH and SI

## Slide 19
pH increases, but with a pause around 5.2
Notes: Step through the results:
-Ca goes up driven by alpha and vel.
-pH goes up, leveling out at equil
-Al is removed, first at slow rate, then at fast rate
-can be understood in terms of pH and SI

## Slide 20
Al disappears, slow at first then fast
Notes: Step through the results:
-Ca goes up driven by alpha and vel.
-pH goes up, leveling out at equil
-Al is removed, first at slow rate, then at fast rate
-can be understood in terms of pH and SI

## Slide 21
Slow Al disappearance is at low pH and MT limited
Notes: Step through the results:
-Ca goes up driven by alpha and vel.
-pH goes up, leveling out at equil
-Al is removed, first at slow rate, then at fast rate
-can be understood in terms of pH and SI

## Slide 22
Sat. Index tells same story as pH
Notes: Step through the results:
-Ca goes up driven by alpha and vel.
-pH goes up, leveling out at equil
-Al is removed, first at slow rate, then at fast rate
-can be understood in terms of pH and SI

## Slide 23
Both slow and fast Al removal are MT limited
Notes: Step through the results:
-Ca goes up driven by alpha and vel.
-pH goes up, leveling out at equil
-Al is removed, first at slow rate, then at fast rate
-can be understood in terms of pH and SI

## Slide 24
This example simulation is much longer than Swank
Notes: Step through the results:
-Ca goes up driven by alpha and vel.
-pH goes up, leveling out at equil
-Al is removed, first at slow rate, then at fast rate
-can be understood in terms of pH and SI

## Slide 25
Model parameterization
Power Law for a:
Global Fitting:

## Slide 26
Model Validation: Works for D Al and Ca

## Slide 27
Model Validation: Not as good for pH, but elevating initial PCO2 helps
PCO2 = 10-3.5 atm
PCO2 = 10 atm

## Slide 28
So, is limestone treatment of AMD MT limited?
Probably
literature on calcite dissolution
low pH Al removal
able to fit Ca and Al w/ single parameter
But
existence of several potential rate limiting steps
gas exchange
other metals
precipitates, scale formation, clogging

## Slide 29
Outline
Background on mass transfer in calcite dissolution kinetics
Data from an open limestone channel (OLC)
Modeling an OLC assuming MT limited kinetics
Speculation about channel geometry in OLC performance
Points of application

## Slide 30
Assume a rectangular channel…
B
y
Fixed Flow Rate
Constant Surface Area
Manning’s Equation Governs Depth
MT Governed by Correlation

## Slide 31
Wider channel is shallower, but vel. hits a max

## Slide 32
At BHS, tres is min and kmt is max

## Slide 33
Combined effect of tres and kmt? BHS is Optimum

## Slide 34
Outline
Background on mass transport in calcite dissolution kinetics
Data from an open limestone channel (OLC)
Modeling an OLC assuming MT limited kinetics
Speculation about channel geometry in OLC performance
Points of application

## Slide 35
Published lab rates will tend to over-predict field rates
“Bucket tests” will tend to under-predict field rates
Anoxic Limestone Drains will have an optimum velocity
Flushable Limestone Beds will be influenced by rate of filling and flushing
If limestone-based treatment is MT limited, then:

## Slide 36
Acknowledgments
Art Rose – Field Data
Ed Zovinka – Column Data (not shown but also supporting MT limits)
Sergio Carvajal – Tracer Tests
David Madl – Early Model Development
SFU’s Center for Watershed Research and Service
Clearfield Creek Watershed Association

## Slide 37
Questions?

## Slide 38
Backup Slides

## Slide 39
Al is removed at a “low” pH
Change in [Al] (mg/L)
pH