## Slide 1: Spaghetti Hole: Retrofit Options for an Aging Passive Treatment System
Jack Gaughan, Nick McKnight, Logan Madison,
Travis Tasker PhD, Jim Eckenrode, Bill Strosnider PhD
ASMR Annual Meeting
Big Sky, MT
June 5th, 2019
Notes: JG

## Slide 2: Outline
Site History
Project Introduction
Sampling and Data Collection
Field & Lab Work
Site Evaluation
Choosing & Finalizing Design Solution
Cost Analysis
Grant Proposal
Notes: LM

## Slide 3: Senior Capstone Project

## Slide 4: Spaghetti Hole, an aging AMD treatment system
Passive treatment system
Located in the Glenwhite Watershed
1 of 6 passive treatment systems
Constructed in 2002 by DEP
Approximately 20 year lifespan
Maintained by the Altoona Water Authority (AWA)
Notes: LM

## Slide 5: Introduction to the Project
Evaluate existing system:
  Determine the efficiency of the existing system
  Assess mass loading of metals from the treatment system utilizing field data
Design solution:
  Identify problems with the existing passive treatment system
  Propose a new design to improve treatment performance
Funding Opportunities
  Growing Greener Grant
Notes: LM

## Slide 6: Existing Site
Plan View
Isometric View
Stabilization Basin
Vertical Flow Pond
Wetland Pond
Stabilization Basin: Large unused area where water flows and no reactions occur
Vertical Flow Pond: Anoxic basin filled with limestone and organic layer
  Sulfate reducing microorganisms use the sulfate in water and organic layer to convert metals to metal sulfides
Notes: nm

## Slide 7: Sampling & Data Collection
Notes: LM

## Slide 8
Chart: [Fe] (mg/L)
[Fe] Assessment Comparing Influent & Effluent Water Quality
Secondary MCL (0.3 mg/L)
Notes: Title & Trendline

## Slide 9
[Al] Assessment Comparing Influent & Effluent Water Quality
Chart: [Al] (mg/L)
Secondary MCL (0.2 mg/L)

## Slide 10: Overflow System

## Slide 11: Relative Percentage of Water Bypassing System
Chart: 
| 43416 | 43418 | 43423 | 43437 | 43446 | 43481 | 43491 | 43502
Relative Overflow | 0.36412 | 0.37859 | 0.48264 | 0.63976 | 0.32985 | 0.64209 | 0.45951 | 0.64639

## Slide 12: Mass Loading of Constituents in Overflow
Chart: Loading (lbs/yr)
Al | 5517.7931
Fe | 634.7451

## Slide 13: Selecting Possible Solutions for the Spaghetti Hole System Based on Influent Water Quality
Skousen, J., et al. Mine Water Environ (2017) 36: 133. https://doi.org/10.1007/s10230-016-0417-1
Notes: NM: Skousen, J., Zipper, C.E., Rose, A. et al. Mine Water Environ (2017) 36: 133. https://doi.org/10.1007/s10230-016-0417-1

## Slide 14: Option 1: Mixed VFP Upgrading the Spaghetti Hole Vertical Flow
Mixing the organic layer and the limestone
  Keep permeability of organic layer
  Keep pH in range to maintain efficiency of sulfate bacteria
Notes: NM: JLN Engineering’s idea is to reduce the amount of limestone present and increase the organic layer, to aim to uniformly increase the pH of the system and decrease the potential for dead zones. Also changing the ratio of the organic layer to limestone will help to keep the focus on using the sulfate reducing bacteria to create metal sulfides that can precipitate and fall out of solution when exposed to the atmosphere. Unfortunately because of the pH problems with Al precipitating out at the perfect range that the Sulfate reducing bacteria are most efficient, a flushing system will need to be used, similarly to the system being used right now, to remove the aluminum that will inevitably build up. Looking forward this is a great technology that can be used, but more information is going to need to be uncovered and some wrinkles ironed out.

## Slide 15: Option 1: Mixed VFP
Benefits
Relatively cheap solution
Less system downtime
Adequate water treatment
Drawbacks
Clogging of organic layer / underdrainage
Generation of nutrients downstream
Added cost of new organic layer

## Slide 16: Option 2: AFLB Retrofit Automatic Flushing Limestone Basin
Choosing a Location
  Important to place:
    After the stabilization basin
    Before the sedimentation basin
Automatic Flushing Limestone Basin
  Periodic flushing to treat aluminum and iron
Notes: LM

## Slide 17: Option 2: AFLB
Benefits
Successfully raises the alkalinity and pH
Effectively removes aluminum
Limestone is present at site
Smaller footprint
Drawbacks
System downtime during construction
Relatively more expensive
Limited space
More earthwork

## Slide 18: Sizing AFLB: Bench Scale Bucket Testing

## Slide 19: Determining a Retention Time
Chart: Time (min)
| 15 | 30 | 45 | 60 | 75 | 90 | 105 | 120 | 135 | 195 | 255 | 315 | 375
Bucket 1 | 5.7 | 5.99 | 5.75 | 5.81 | 5.89 | 6.06 | 6.09 | 6.23 | 6.3 | 6.39 | 6.49 | 6.73 | 6.74
Bucket 2 | 5.84 | 6.04 | 6.16 | 6.22 | 6.32 | 6.37 | 6.45 | 6.5 | 6.6 | 6.62 | 6.69 | 6.73
Bucket 3 | 5.83 | 5.95 | 6.11 | 6.15 | 6 | 6.32 | 6.42 | 6.45 | 6.58 | 6.62 | 6.57 | 6.68
Chart: Time (min)
| 15 | 30 | 45 | 60 | 75 | 90 | 105 | 120 | 135 | 195 | 255 | 315 | 375 | 435
Bucket 1 | 32.5 | 38 | 51.5 | 50 | 54.5 | 51.5 | 111 | 130.5 | 134.5 | 142 | 152 | 188 | 192 | 170.5
Bucket 2 | 52 | 49.5 | 54.5 | 58 | 62.5 | 153 | 162 | 170.5 | 176 | 183 | 186.5 | 190 | 179
Bucket 3 | 46 | 49.5 | 53.5 | 57.5 | 60.5 | 149.5 | 146.5 | 155 | 162.5 | 174.5 | 174 | 173.5 | 198

## Slide 20: Discussing Solubility & Speciation of [Al] with respect to pH

## Slide 21: AutoCad: Existing Site
Stabilization Basin
Vertical Flow Pond
Wetland
Stabilization Basin
Sedimentation Basin
Automatic Flushing Limestone Basin
Wetland
AutoCad: Proposed Site
Notes: NM

## Slide 22: AutoCad: Proposed Stabilization Basin
Stabilization Basin
  Moving the organic layer from the VFP to the stabilization basin
    Shrink the volume of the basin from 70,000 cubic ft to 30,000 cubic ft
  Moving the organic layer to a new site
Before
After
Notes: NM

## Slide 23: AutoCad: Automatic Flushing Limestone Basin
After
Automatic flushing limestone basin:
  Limestone increases alkalinity and pH of the water
  Increased pH reduces metal solubility resulting in metal hydroxide precipitate
Before
Notes: NM

## Slide 24: Inflow Structure to Limestone Bed

## Slide 25: Automatic Flushing Device

## Slide 26: AutoCad: Sedimentation Basin
Stabilization Basin
Sedimentation Basin
Automatic Flushing Limestone Basin
Wetland
Sedimentation Basin:
  Slow flow allows solid metal hydroxide to settle
  Meander to increase time for settling to occur
After
Before
Notes: NM

## Slide 27: Outlet Structures in Tandem

## Slide 28: AutoCad: OverFlow Structure Cross Section
Sedimentation Basin
Automatic Flushing Limestone Basin
Wetland
Notes: NM

## Slide 29: Level Pool Routing: Sedimentation Basin

## Slide 30: AutoCad: Wetland
Before
After
Wetland:
  Forebay to catch the flushed metal solids
  4 ft deep to stop cat tail growth
  Approximately 25% of width of site based on in-wetland-plant-growth
  Magnanese removal option with limestone implimentation
Notes: NM

## Slide 31: Cost Analysis
Construction
  Site inspection
  Earth work
  Limestone
  PVC piping - underdrainage
  Outlet structures - agri drain, floating outlet structure and weir
  E & S control and seeding/mulching
  PVC underdrainage removal
  Access road
Notes: LM

## Slide 32: Reuse of On-site Materials
Limestone rock currently in the VFP
  Total Quantity Present: 3,538 yd3
Limestone to be placed in the automatic flushing limestone basin
  1,308 yd3
Left over limestone
  3,538 yd3 - 1,308 yd3 = 2,230 yd3
  Can be used on the access road, diversion channels, etc.
Notes: LM

## Slide 33: Access Road Breakdown
Notes: LM

## Slide 34: Cost Analysis
Project Component | Cost
Mobilization & Demobilization | $2,000
Construction | $136,500
Engineering (10%) | $13,800
Maintenance | $1500 - $15,000
TOTAL | $153,000
Notes: LM
Round the numbers

## Slide 35: Final Deliverable: Growing Greener Grant
Growing greener grant
  Detailed project description
  Justification of funding
  Scope of work
  Cost
  Signed letters of commitment

## Slide 36: Thanks to...