## Slide 1
Soil Water Chemistry of Reforested Mine Site in West Virginia
Amir Hass
West Virginia State University
ASMR, June 3-7, 2019. Big Sky, MT

## Slide 2
EPA. 2011. “The Effects of Mountaintop Mines and Valley Fills on Aquatic Ecosystems of the Central Appalachian Coalfields”, EPA/600/R-09/138F March 2011.
Coal Mining - Mountaintop Removal Operation

## Slide 3
Skouson et al., 2011. Forest Reclamation Advisory No. 8, ARRI
Gray Sandstone
Native vegetation & landscape
Native soil
Brown Sandstone
Typical Overburden Stratification

## Slide 4
Skouson et al., 2011. Forest Reclamation Advisory No. 8, ARRI
Placement of Topsoil Replacement Material
Brown Sandstone Plot

## Slide 5
Catenary Mine Site – Field Plots

## Slide 6
Brown
Sandstone plot
Non compacted
Compacted
Gray Sandstone plot
Non-compacted
Compacted
Catenary Mine Site – Field Plots
100 m

## Slide 7
Brown
Sandstone plot
Gray Sandstone plot
Catenary Mine Site – Field Plots
March 2017

## Slide 8
Objectives
Evaluate the mid-term impact of Forestry Reclamation Approach Practices on Soil Water Chemistry:
Effect of spoil type (brown vs. gray sandstone)
Effect of spoil placement practice (loose vs. compacted)

## Slide 9
115cm long, 5-cm ⌀ PVC pipe
2-cm perforated band @15cm from the bottom (water collected @ depth of 85 cm)
Catenary Mine Site – Well Locations
March-April 2017
Acid-washed quartz sand layer put around perforated band
2-cm layer of bentonite to cap the well at the surface
Hole refilled with dugout material
Well is crowned at the surface

## Slide 10
Catenary Mine Site – Pan Installation

## Slide 11
Brown
Sandstone plot
Non compacted
Compacted
Gray Sandstone plot
Non-compacted
Compacted
100 m
Catenary Mine Site – Wells Location

## Slide 12
Catenary Mine Site – Water Sampling
Water level
YSI Multi-probe (Temp, EC, ORP, DO)
ICP
(Acidified sample 4% HNO3)
(Al, As, Ba, Ca, Cd, Co, Cr, Cu, Fe, K, Mg, Mn, Mo, Na, Ni, P, Pb, S, Se, Zn)
Ionic composition
(Li, Na, NH4, Ca, Mg, K; F, Cl, NO2, Br, NO3, PO4, SO4)
TC
(sealed, no headspace)
Water Sampling
(filtered <0.45 µm)
Total Alkalinity
(sealed, no headspace)
Chart: Volume of HCl added (mL)
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.85 | 0.9 | 0.95 | 1 | 1.05 | 1.1000000000000001 | 1.1499999999999999 | 1.2 | 1.25 | 1.3 | 1.35 | 1.4 | 1.45 | 1.5 | 1.55 | 1.6 | 1.65 | 1.7 | 1.75 | 1.8 | 1.85 | 1.9 | 1.95
 | 10.993 | 10.604 | 10.242 | 9.825 | 8.836 | 7.012 | 6.518 | 6.097 | 5.471 | 4.276 | 3.273 | 2.989 | 2.822 | 2.701 | 2.607 | 2.519 | 2.455 | 2.403 | 2.353 | 2.311 | 2.271 | 2.236 | 2.203 | 2.172 | 2.144 | 2.116 | 2.091 | 2.069 | 2.046 | 2.026 | 2.005 | 1.986
 | 0.0042823 | 0.043147 | 0.083027 | 0.12204 | 0.16134 | 0.20046 | 0.24563 | 0.28481 | 0.32124 | 0.36065 | 0.39752 | 0.43614 | 0.47303 | 0.51069 | 0.54881 | 0.58572 | 0.62511 | 0.66256
Notes: Alk by gran plot on filtered sample with no head space; ICP on acidified sample (4% concentrated HNO3); TC analysis (Aurora 1030W Total Organic Carbon Analyzer) followed by Dionex ICS 1100)

## Slide 13
Results
Chart: pH
Gray | 76 | 241.9 | 125.5 | 382.3 | 263 | 632 | 605 | 683 | 638 | 534 | 339.5 | 438.1 | 64.5 | 56.5 | 178.1 | 71.1 | 267.3 | 231.9 | 156.4 | 98.6 | 87.8 | 80.3 | 86.6 | 70.4 | 65.2 | 151.5 | 170.3 | 194.6 | 103.8 | 66.6 | 102.8 | 209.6 | 163 | 71.2 | 82.1 | 82.9 | 83.4 | 101.2 | 135.2 | 227.2 | 199.8 | 182.2 | 206.6 | 202.6 | 214.2 | 218.5 | 168.6
Native | 496.4 | 268.3 | 406.4 | 187.1 | 187.6 | 335.9 | 261.2 | 360.5 | 401.5 | 321.9 | 31 | 38.2 | 71.4 | 66.2 | 47.6 | 47.5 | 208 | 90.2 | 122.1 | 113.1 | 130.3 | 213.2 | 229.2 | 225.5
surface | 328.5 | 36 | 21.6 | 22.2 | 17.3 | 14.7 | 35.6 | 63.5 | 64.3 | 51.7 | 31.1 | 50.2 | 33.2 | 47.1 | 36.2 | 76.6 | 59.5 | 47 | 44.4
pH – EC relationships
Notes: Update values; include ratio

## Slide 14
pH – Eh relationships
MnO2 + 4H+ + 2e- → Mn2+ + 2H2O
Fe(OH)3 + 3H+ + e- → Fe2+ + 3H2O
NO3- + nH+ + ne- → N2, N2O + H2O
SO4-2 + 8H+ + 6e- → S + 4H2O
CH3OH + 2H+ + e- → CH4 + H2O
Reduction Reactions – pH ↑
CO2 (from aerobic through methanogenic environment) → carbonic acid → pH ↓
Microbial Redox Reaction product:
Results (Cont.)
Chart: pH
gray | 340 | 379.9 | 389.9 | 378.9 | 343 | 324 | 118.7 | 310.6 | 352.9 | 349 | 317.9 | 276.5 | 379 | 383.7 | 371.5 | 338.6 | 328.7 | 294.5 | 272.7 | 267.3 | 278.1 | 299.4 | 333.4 | 284.9 | 324 | 329.7 | 373.8 | 305.8 | 247.5 | 426.3 | 346.3 | 344.7 | 324.8 | 253.4 | 284.1 | 331 | 442.5 | 371 | 356.2 | 305.2 | 331 | 337.2 | 340.5 | 349.2 | 269.7 | 332.3 | 256.4
native | 388.7 | 340.8 | 335.2 | 404.6 | 395.3 | 386.8 | 394.2 | 345.9 | 339.4 | 345.8 | 406.1 | 353.6 | 350.9 | 346 | 393.4 | 402.8 | 347.1 | 335.7 | 400.6 | 358.6 | 309.1 | 344.4 | 325.9 | 344.4
surface | 409.9 | 370.5 | 337 | 323.1 | 344.5 | 371.9 | 217.2 | 339.8 | 345.9 | 373.1 | 351.5 | 349.7 | 347.6 | 320 | 335 | 336.5 | 321.8 | 306.5 | 318.9

## Slide 15
Results (Cont.)
Chart: pH
Chart: 
| 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9
EC | 60.8 | 113.8034 | 228.9765 | 292.85 | 345.3324 | 269.425 | 134.2857 | 72.1333
Eh | 380.94 | 376.731 | 312.9559 | 275.0152 | 261.5044 | 313.6194 | 326.0667 | 319.7333
Eh and EC are inversely related
EC (uS cm-1)
Eh (mV)
pH
Notes: Avg of Eh (2ndary axis) and EC within 0.5 pH increments

## Slide 16
TDS (µS cm-1)
pe
Chart: 
Results (Cont.)

## Slide 17
Results (Cont.)
Chart: pH
gray | 340 | 379.9 | 389.9 | 378.9 | 343 | 324 | 118.7 | 310.6 | 352.9 | 349 | 317.9 | 276.5 | 379 | 383.7 | 371.5 | 338.6 | 328.7 | 294.5 | 272.7 | 267.3 | 278.1 | 299.4 | 333.4 | 284.9 | 324 | 329.7 | 373.8 | 305.8 | 247.5 | 426.3 | 346.3 | 344.7 | 324.8 | 253.4 | 284.1 | 331 | 442.5 | 371 | 356.2 | 305.2 | 331 | 337.2 | 340.5 | 349.2 | 269.7 | 332.3 | 256.4
native | 388.7 | 340.8 | 335.2 | 404.6 | 395.3 | 386.8 | 394.2 | 345.9 | 339.4 | 345.8 | 406.1 | 353.6 | 350.9 | 346 | 393.4 | 402.8 | 347.1 | 335.7 | 400.6 | 358.6 | 309.1 | 344.4 | 325.9 | 344.4
surface | 409.9 | 370.5 | 337 | 323.1 | 344.5 | 371.9 | 217.2 | 339.8 | 345.9 | 373.1 | 351.5 | 349.7 | 347.6 | 320 | 335 | 336.5 | 321.8 | 306.5 | 318.9
Oxic
Suboxic
Anoxic
Notes: Update values; include ratio

## Slide 18
Chart: SO4 (mg L-1)
| 2.1906693711967544 | 1.7224475997295472 | 1.2457741717376607 | 1.125760649087221 | 1.4705882352941178 | 1.440162271805274 | 1.5365111561866127 | 1.5483434753211629 | 1.6531440162271807 | 1.7866801893171063 | 2.8093306288032456 | 4.4455713319810686 | 4.5419202163624073 | 5.4851250845165653 | 6.1308316430020282 | 0.90939824205544306 | 3.2910750507099391 | 3.4448951994590944 | 3.532792427315754 | 5.2586206896551735 | 4.9425287356321839 | 5.1233941852603113 | 4.4641649763353621 | 4.9797160243407719 | 5.9617985125084516 | 6.1916835699797161 | 5.2129817444219064 | 6.2339418526031105 | 5.3498985801217041 | 5.2636916835699799 | 4.3103448275862073 | 5.0236646382691008 | 4.9459093982420566 | 4.4895199459093993 | 4.5486815415821509 | 5.7572684246112242 | 5.5375253549695751 | 5.552738336713996 | 5.7200811359026371 | 5.9617985125084516 | 6.4232589587559161 | 5.2129817444219064 | 5.0422582826233944 | 4.4844489519945911 | 3.8184584178498988 | 3.8235294117647061 | 4.2359702501690331 | 4.1413116970926307 | 3.7390128465179173 | 4.1970926301555105 | 4.215686274509804 | 4.0094658553076403 | 3.2792427315753891 | 5.3853955375253557 | 3.443204868154158 | 3.7880324543610548 | 4.1717376605814742 | 5.1149425287356332 | 5.4259634888438137 | 5.1842461122379984 | 5.963488843813388 | 3.98580121703854 | 5.6000676132521976 | 4.4658553076402976 | 5.45131845841785 | 5.0169033130493581 | 5.0676132521974315 | 5.1893171061528065 | 6.0767410412440839 | 3.1558485463150778 | 4.1311697092630162 | 3.2809330628803246 | 3.4482758620689657 | 2.9716024340770795 | 3.0054090601757948 | 3.052738336713996 | 2.9716024340770795 | 3.111899932386748 | 3.8877620013522654 | 2.9344151453684924 | 2.0554428668018931 | 2.6538201487491548 | 2.7298850574712645 | 2.6994590939824206 | 3.010480054090602 | 3.2893847194050037 | 5.5628803245436114 | 3.9891818796484113 | 3.3181203515889117 | 3.040906017579446 | 5.3921568627450984 | 3.061189993238675 | 4.7041920216362412 | 5.3752535496957403 | 5.2721433400946589 | 4.9526707234617984 | 5.9465855307640298
W1 | 10.3003 | 0 | 0.6129 | 6.835 | 5.1442 | 8.987 | 4.0375 | 10.8472 | 18.2699 | 75.0282 | 85.5174 | 96.8292 | 67.4067 | 65.892
pe
pe, Conductivity, and Ionic Composition
Results (Cont.)

## Slide 19
Chart: 
pe, Conductivity, and Ionic Composition
SO4-2
TDS (µS cm-1)
(mg L-1)
Results (Cont.)
pe <2

## Slide 20
Hypothesis: TEA abundance will govern solution redox potential
H2O
H2
O2
H2O
NO3-
N2
MnO2
Mn2+
Fe(OH)3
Fe2+
SO42-
H2S
CO2
CH4
Incubation Study - Effect of terminal electron acceptor on redox potential

## Slide 21
Hypothesis (cont.): Such effect will be more pronounce in soil of limited/initial pedogenic (soil development) stage
Incubation Study - Effect of terminal electron acceptor on redox potential
Meaning, we expect that ‘topsoil replacement material’ (i.e. crushed rock) contain limited pool(s) of available TEA

## Slide 22
Chart: Fe (mg kg-1)
| CD | AAO | CD | AAO | CD | AAO | CD | AAO | Brown | Gray | Undisturbed | BC6
Fe | 2228.4123 | 1059 | 1049.4307 | 1568.0628 | 2606.9345 | 1604.034 | 748.8924 | 5120.6356
Free Iron Oxides Content in Soil and Rock Material

## Slide 23
Incubation Study - Effect of terminal electron acceptor on redox potential
Soil Type (3):
Gray Sandstone
Brown Sandstone
Native Soil
Terminal e- Acceptor (4; 5.0mM):
NO3
SO4
Fe2O3
None
Notes: 6 different solutions: no terminal electron acceptor (#1) and with NaNO3 (#2), NaSO4 (#3), MnO2 (#4), Fe2O3 (#5), and a mix of all reagents (#6). Different amount of CaCl2 (as CaCl2·2H2O) was added to each solution of no terminal e- acceptor and that of NaNO3, NaSO4 to reach a common targeted total salt concentration and EC.

## Slide 24
Results (Cont.)
Incubation Study - Effect of terminal electron acceptor on redox potential
Chart: Gray
| 0 | 25 | 50 | 75 | 100
NO3 | 455.8 | 261.04 | 159.24 | 201.6 | 227.74
SO4 | 407.8 | 264.9 | 190.86 | 179.7 | 199.8
Fe | 507.9 | 316.76 | 190.28 | 214.8 | 195.72
none | 424 | 214.1 | 246.84 | 228.2 | 230.46

## Slide 25
Results (Cont.)
Incubation Study - Effect of terminal electron acceptor on redox potential
Chart: Brown
| 0 | 25 | 50 | 75 | 100
NO3 | 450.6 | 295.32 | 271.4 | 235 | 252.68
SO4 | 431.1 | 245.6 | 168.32 | 146.3 | 178.38
Fe | 504.3 | 311.02 | 129.7 | 169.96 | 159.82
none | 449.5 | 286.2 | 260.18 | 282.18 | 314.28

## Slide 26
Results (Cont.)
Incubation Study - Effect of terminal electron acceptor on redox potential
Chart: Native
| 0 | 25 | 50 | 75 | 100
NO3 | 420.3 | 281.42 | 187.66 | 145 | 142.56
SO4 | 413.9 | 32.2 | 55.5 | 89.05 | 89.175
Fe | 473.3 | 208.46 | 138.02 | 149.22 | 155.34
none | 426.1 | 166.76 | 144.28 | 155.62 | 169.84

## Slide 27
Results (Cont.)
Incubation Study - Effect of terminal electron acceptor on redox potential (25 day)
(Native soil)
Chart: Terminal Electron Acceptor
| NO3 | Fe | none | SO4
 | 281.42 | 208.46 | 166.76 | 32.2
b
b
c
NO3 > Fe ≈ None >> SO4

## Slide 28
Redox reactions dominated solution properties, affecting solution pH and composition.
High TDS associated with low pe
Summary
Reductive dissolution (as opposed to acid dissolution) likely play a significant role in producing excess TDS (though this is likely more complex than any binary system/choice)
Abundance of TEA (e.g. SO4) may govern/maintain low(er) redox potential (that could otherwise be assumed judging from soil/site moisture regime)

## Slide 29: Acknowledgements
Jeff Skousen, WVU
Robert Cantrell, John Lucas, Zac Lucas, Tigist Geberehiwot, Jake Harms, Edgar Lopez, Rein Yousef, Kim Cavender, Fatima Irfan
Kenny Daniel (ERP Environmental Fund, Inc.)
Randall Lester, Warren Haynes (USDA NRCS PMC, Alderson WV)
Funding Agencies: