## Slide 1: TAILINGS BASIN RECLAMATION ATLANTIC CITY IRON MINE, WYOMING
WYOMING AML PROJECT 9A-II
J. J. Gusek P.E., Linkan Engineering, Golden, CO
&
B.K. Schladweiler, BKS Environmental, Gillette, WY

## Slide 2: Site Location
Southern end of the Wind River Mountains
35 mi south of Lander WY on South Pass (WY Highway 28)

## Slide 3: SITE HISTORY
Iron resource recognized during Cold War
This mine and the Sharon Steel Mill in SLC were located out of range of ICBMs at the time.
US Steel operated mine 1962 to 1983
Salvage operator acquired property in about 1985 for railroad rails but later sold
WY AML assumed some of reclamation responsibility in late 1980’s

## Slide 4: Site Environment
  Site elevation – 8,100 ft (2,470 m)
  Strong winds
  Short growing season
  Semi-arid/high altitude climate

## Slide 5: SITE SPECIFIC PROBLEMS Prior to Reclamation
A tailings basin cap installed in 1985 was being eroded by uncontrolled ground water seeps
Wind-blown dust from the tailings basin was causing zero visibility on adjacent state highway to the south

## Slide 6: Challenges
Site conditions described previously
On-going drought during construction and reclamation
  8-year drought
  Most intense period August 2002
No topsoil originally salvaged/source of borrow topsoil

## Slide 7: SITE LAYOUT
Relocated HWY 28 (2003?)

## Slide 8: Seeps eroding vegetative cover soil
SEEPAGE FROM PIT LAKE

## Slide 9: Mill and Tailings Basin 1994
Seeps
Partly Revegetated
Exposed Tailings
Tailings Pond discharging through decant tower

## Slide 10: WY AML’s Responsibilities
Reclaim lands not covered by owner obligations
  Tailings Basin Reclamation
  Portions of Waste Rock Dumps
  Railroad Bridge Abutments
  Railroad Fill Removal/Breaching
Notes: DELETE?

## Slide 11: INITIAL PROJECT GOALS
Provide a stable reclaimed surface to prevent blowing dust and develop habitat for wildlife and cattle grazing
Preserve or improve the stormwater protection the mine pit and tailings basin provided to downstream communities, especially during construction

## Slide 12: PRE-DESIGN INVESTIGATIONS
Geotechnical - 2 tailings dams (North and South)
Site geochemistry
Surface water hydrology
Feasibility of compost use
Soils and revegetation
Threatened & endangered species
Notes: DELETE?

## Slide 13: General Reclamation

## Slide 14: RECLAMATION PLAN

## Slide 15: Site Features prior to Fall 1997 Seeding

## Slide 16: Reclamation Plan Specifics
Rock wall snow fences substituted for vertical slat snow fences
Fertil Fiber/Kiwi-Power amendments with nearby White River overburden substituted for organic compost or imported topsoil
  Based on historical research of taconite tailings
  WRF low fertility but no chemical limitations (neutral pH; As <2 mg/kg)
Broadcast seed
Plant adapted species @ 40 kg/ha PLS (35-36 lbs/ac)

## Slide 17: SOIL AMENDMENTS
(DRY) Fertil Fibers/Biosol applied in two doses @2.2 t/ha (1.0 st/ac) with dry inorganic fertilizer supplement
(WET) Kiwi Power bacterial inoculum applied at 47 liters/ha (5 gallons/acre) applied with “crop duster” airplane.

## Slide 18: Fertilizer
Diammonium phosphate fertilizer 250 lb/acre
  45 lbs elemental N
  115 lbs elemental P
Potash 36 lb/acre
  30 lbs elemental K

## Slide 19: Mulching
Other than hydroseeded/hydromulched areas, no mulching was used

## Slide 20: Seed Mix – Drill Rate
Critana Thickspike 3.0 PLS/ac
Rosana Western 3.0 PLS/ac
Secar Bluebunch 3.0 PLS/ac
Bromar Mountain Brome 4.0 PLS/ac
Trailhead Basin Wildrye 2.0 PLS/ac
Joseph Idaho Fescue 2.0 PLS/ac
Appar Blue Flax 0.5 PLS/ac
Eski Sanfoin 2.0 PLS/ac
Mountain Big Sagebrush 1.0 PLS/ac
TOTAL 17.5 PLS/ac

## Slide 21: Fencing
Cattle grazing excluded for two growing seasons
Wildlife grazing could not be economically excluded

## Slide 22: CONSTRUCTION SCHEDULE
Dec, 1996 - Winter startup/regrading of initial tailings basin
Nov, 1997 - Winter weather suspends revegetation work
Spring, 1998 – revegetation work complete, regrade other sites in project
Notes: DELETE?

## Slide 23: Tree Planting
Conducted in 2001
Two tree species in wind shadows of rock berms and rock boulder snow fences (15,000 trees)
Used 2’ x 2’ black matting
Lodgepole and limber pines – seeds harvested from forest within 500 feet of the mine and grown in containers in a CO nursery
Installed browse protection sleeves

## Slide 24: Reclamation Sequence

## Slide 25: Reclamation Project Areas/Phases
Tailings Storage Facility (TSF) (impoundment) including tree planting – Phase 1
RR bridge abutment removal – Phase 1A
Waste rock dumps – Phase 2
Railroad fill breaching – Phase 3

## Slide 26: SITE LAYOUT
Relocated HWY 28 (2003?)

## Slide 27: Challenges
New spillway 10 ft lower than the normal Iron Lake level.
  Constructing the spillway without creating a flood was a challenge.
  However, as excavation occurred closer to the Lake, the “seepage” encountered increased so that the lake level dropped in a controlled fashion.
Seep flow on the north end of the TSF managed with French Drains that daylighted at the tailings pond shoreline

## Slide 28: Iron Lake to Tailings Pond Spillway
Iron Lake
Tailings Pond
New Spillway
Iron Lake water level 10 ft. lower to eliminate seeps)

## Slide 29: French Drains (more seep control)

## Slide 30: Closure of Lower Diversion Canal/Old Spillway
Iron Lake
Tailings Pond
Lower Diversion Canal Alignment
Old Spillway
French Drains
Tailings Dam

## Slide 31: New Tailings Basin Spillway
Iron Lake
Tailings Pond
New Spillway
French Drains
Tailings Dam

## Slide 32: Tailings Basin Post-Construction
Tailings Pond
Iron Lake Spillway
Rock Boulder Snow Fence
Buried French Drains in this area

## Slide 33: Tailings Basin + 2 yrs.
Tailings Pond
Iron Lake Spillway
Buried French Drains in this area

## Slide 34: Tree Planting Assessment on Tailings Basin
Used Google Earth Imagery to count trees around 36 rock boulder snow fences
  Used to determine tree survival rate
  Lowest survival rate at a rock boulder snow fence was 11%
  Highest survival rate at a rock boulder snow fence was 80%
  Average survival rate at a rock boulder snow fence was 41%

## Slide 36: Overall Statistics
 | Tree Count |  | Tree Mats |  | Survival Rate
Minimum | 4 |  | 28 |  | 11.4%
Average | 48.9 |  | 116.7 |  | 41.4%
Maximum | 145 |  | 333 |  | 79.7%
*Total | 1,760 |  | 4,201 |  | 41.9%
36 structures/polygons sampled * All trees and tree mats sampled. Accounts for the difference between the average and total survival rates. Reportedly, 15,000 trees were planted so the overall survival rate would be about 12% |  |  |  |  | 
What happend?
Notes: Average was calculated by taking the average survival rate of each polygon. The Total was the sum of all trees counted, all tree mats counted, and the difference for the average (Average=total trees counted divided by total tree mats counted.
What happened? Here’s a theory…

## Slide 37: Big Sagebrush – NE of tailings basin
NE of tailings basin
Simultaneously broadcasted shrub seed within drill seeded grasses

## Slide 38: Reclamation Project Areas/Phases
Tailings Storage Facility (TSF) (impoundment) – Phase 1
RR bridge abutment removal – Phase 1A
Waste rock dumps – Phase 2
Railroad fill breaching – Phase 3

## Slide 39: Bridge Abutment (Highway Hazard) Removal
Phase 1A

## Slide 40: Hazards
Long considered a “choke point” on a long downhill stretch of highway that, under wintery conditions, could have resulted in a fatality if a vehicle hit the abutments.
The abutments were also considered a hazard to snowmobilers who routinely used the railroad right of way.
WY AML elected to have them removed.

## Slide 41: Bridge Abutment Removal
Phase 1A
Photos courtesy of Tim Richmond, WY AML (retired)
Notes: The bridge abutment removal involved the use of explosives and the demolition contractor’s blaster was a bit trigger happy on the first few shots and the highway was closed for six hours! People weren’t very happy. Eventually, the blaster got the hang of it and the closures were less than 45 minutes. The Google Earth street view shows very mature vegetation – you’d never know what had been there.

## Slide 42: Reclamation Project Areas/Phases
Tailings Storage Facility (TSF) (impoundment) – Phase 1
RR bridge abutment removal – Phase 1A
Waste rock dumps – Phase 2
Railroad fill breaching – Phase 3

## Slide 43: SITE LAYOUT
Relocated HWY 28 (2003?)

## Slide 44: Considerations
While the un-reclaimed waste rock areas presented no physical hazards, their reclamation was within AML’s mission statement.
Some of the advancements on the tailings project were transferred to the waste rock projects (e.g., rock snow fences)

## Slide 45: Waste Rock Reclamation (Phase 2)
Ripping and Final Shaping

## Slide 46
Atlantic City: Phase 2 (con’t)
Placing Cover Materials on Waste Dumps

## Slide 47: Incorporating Soil Amendments and Fertilizers
Atlantic City: Phase 2 (con’t)
Notes: Soil amendments included a combination of slow-release fertilizer and a soluble liquid fertilizer for immediate plant utilization.

## Slide 48
Pitted Surface on Slopes
Improves soils moisture capture and retention
Reduces wind erosion and abrasion of young seedlings

## Slide 49
Atlantic City: Phase 2 (con’t)
Hydroseeding

## Slide 50: Reclamation Project Areas/Phases
Tailings Storage Facility (TSF) (impoundment) – Phase 1
RR bridge abutment removal – Phase 1A
Waste rock dumps – Phase 2
Railroad fill breaching – Phase 3

## Slide 51: SITE LAYOUT
Relocated HWY 28 (2003?)

## Slide 52: Railroad Fills Removed/Breached
Notes: The railroad fills presented potential flooding hazards if the steel culverts ever failed and water ponded up behind them to eventually fail catastrophically, resulting in loss of life and property. Removing them was a no-brainer for WY AML. (please don’t point out the lack of a hard hat on one of the workers – LOL).

## Slide 53
Railroad Fills Removed/Breached
Railroad Fill Removed
Fill Material Placed to Approximate
Original Contour
Slate Creek
0.25 miles to
Hwy 28 RR Abutments (removed earlier)
Notes: The excavated materials were transported into the cut adjacent to the fill that probably provided the original fill materials.

## Slide 54: Post Seeding Followup

## Slide 55: AML Site Monitoring
2007
Noted:
  Limited success of conifers behind rock habitat structures due to marmot activity
  Main drainage out of Rock Creek blocked by overburden
  Trash and debris in creek
  Loose, resilient weed mats
  Sanfolin, wheatgrass, flax and sagebrush noted
  No noxious weeds

## Slide 56
Near Remaining High Wall
(view south on lower photos)

## Slide 57
Reclaimed Waste Rock Dumps – Note Loose Weed Matting

## Slide 58
East Edge of Main Pit, View South
East Edge of Main Pit, View North

## Slide 59
Downstream From The Outlet Of The Main Pit Pond

## Slide 60
Interrupted Flow from the Rock Creek Reservoir

## Slide 61
Flow of water coming up just above the old highway on the southeast side of the site
Channel structure flowing out of the pond from the previous photo

## Slide 62
Stakes left after the straw bales were likely consumed by livestock

## Slide 63: Contractor Monitoring

## Slide 64: Summary – Observations and Lessons Learned
Dust problem on tailings under control
Stable landforms on tailings, waste rock dumps, railroad fills established
Relocated Highway 28 seems to blend into the landscape
Lessons learned (trees)
  consider small wildlife browsing even with browse protection
  reconsider strategic placement behind rock structures
  were there more conducive areas to tree establishment
  Skip the trees? Plant other species?
  Overall, was it worth it?
Notes: Summarize each bullet

## Slide 65: Questions?
Chance favors the prepared mind.
Louis Pasteur
Special thanks to J.R. Simplot, current mine owner, for permission to visit the site in 2018 and to share this success story.
jim.gusek@linkan.biz
BSchladweiler@bksenvironmental.com
Notes: If there are questions I can’t answer, please feel free to contact Jim at his email address.