## Slide 1: Rumsey Mill & Fred Burr Creek Site Characterization

## Slide 2: Project Members
  Granite Headwaters Watershed Group
    DNRC Grant
  Trout Unlimited
    Project Coordination
  Landowners
  KC Harvey Environmental
    Natural Resource and Technical Lead

## Slide 3: Rumsey Mill & Fred Burr Creek Site Characterization
Project Location

## Slide 4: Site Background
  Mill History
    Milling silver circa 1890’s
    Mercury and metals in tailings
  Substantial Site Disturbance
    Off site Re-processing (historic; 1930’s – 1950’s)
    Pond and ditch construction (circa 1996/97)
    Pond site reclamation (circa 2002/03)
    Subdivision and Development (current)
    Recent fire
    Natural erosion of mill site area and streambanks

## Slide 5: Site Background
  Key Previous Investigations
    Focused on Mill Site area and SW/Sediments
      MDEQ
        AML program (circa 1995)
        SW and Sediments (circa 2015/16)
      EPA (1997 – 2001)
        In response to 404 violation/pond construction
        SW, Sediments, Soils/Tailings
        Ecological Risk Assessment
      Montana FWP (2014)
        BMI’s Private (2002)
        Reclamation of pond construction site
      University of Montana (2014)
        Sediment Sampling

## Slide 6: Existing Data Review (Pre-2018 Field Investigation)
Summary
    Elevated mercury, arsenic and lead in surface water and sediments in Fred Burr Creek below mill site to Flint Creek
    Elevated mercury, arsenic and lead in floodplain soils of Fred Burr Creek around mill site
    Elevated mercury in BMI and fish in Flint Creek
    Eco Risk Assessment - Benthic and terrestrial invertebrates and reference plants impacted
    Mill site area disturbed/reclaimed in some areas of sampling; no post-reclamation confirmation sampling of soils
    Unknown level of soil contamination below historic mill/tailings location on Fred Burr Creek floodplain

## Slide 7: Rumsey Mill circa 1890’s

## Slide 8: Historic Rumsey Mill Site (MBMG)

## Slide 9: Parcel Map of Upper Fred Burr Creek

## Slide 11: Historic Soil Data in Vicinity of Mill and Reclaimed Areas

## Slide 12: Reclaimed Bare/Tailings Areas (left) and Repository (right) (From LMRC and WET, 2003)

## Slide 14: b

## Slide 16: 2017 Data Gaps
Extent (lateral and depth) of contamination
  Limited to historic mill site area
  Many historic land disturbances
Sediment source to Creek
Groundwater Quality and effects on Fred Burr Creek
Roads/Construction materials
Effect of recent flood flows on stream sediment chemistry

## Slide 17: Field Investigation
Objective: Define extent and degree of milling contamination in upper FBC
Sampling and Analysis Plan
  Focused soil/tailings sampling from soil pits in the upper (mill area) FBC floodplain (no access)
  Soil/Tailings sampling from soil pits along transects between mill site and moraine crest
    XRF analysis permits real time decision making and saves $
    Laboratory confirmation samples
  Sediment sampling at select locations (similar to previous efforts)
  Limited co-located surface water samples to correlate to stream sediment results
  Groundwater observations/sampling to:
    Note depth to GW in soil pits
    Install piezometers for seasonal measurements of GW levels

## Slide 18: Sampling Methods
Soil
  11 Hand-dug pits
  39 Mini excavator (larger)
  147 XRF samples from various depths
Sediment
  5 samples from low-energy sections of FBC channel
Surface Water (SW)
  4 samples co-located with sediment samples
Groundwater (GW)
  6 piezometers installed in soil pits

## Slide 19: QA/QC
Soil
  Daily accuracy and precision using NIST Hg standards
  Daily cross-contamination blanks
  11 Field Duplicates
  20 sample splits for lab physical & chemical analyses
Sediment
  1 Field Duplicate
  All samples for lab analyses
  All samples split for fine fraction (< 63um) analysis of Hg
Surface Water (SW)
  1 Field Duplicate

## Slide 20: Fred Burr Creek bench (foreground) and floodplain looking SE

## Slide 21: Typical excavator-dug soil pit during the July 23rd to 26th 2018 field investigation at Fred Burr Creek.

## Slide 22: Watershed-scale site map and sampling locations for the July 2018 field investigation at Fred Burr Creek.
6/17/2019
FBC Data Summary Presentation

## Slide 23: Sampling locations and results summary for July 2018 field investigation in upper Fred Burr Creek.
6/17/2019
FBC Data Summary Presentation

## Slide 24: Representative FBC soil profile and descriptions at sampling pit SP-8 (sharpshooter spade for scale). Inset, lower left: close-up of tailings layer (2-8” BGS) found throughout FBC.
6/17/2019
FBC Data Summary Presentation
0-2” BGS: silty loam; roots/OM
(mg/kg: 90 Hg / 2,593 As / 1,254 Pb)
2-8” BGS: Medium brown very fine (v.f.) sand to silt, no mica (tailings layer— mg/kg: 226 Hg / 8,425 As / 3,084 Pb)
8-16” BGS: Dark brown micaceous v.f. sand to silt (mg/kg: ND<1.8 Hg /
85.0 As / 9.5 Pb)
16-23” BGS: Interbedded fine to medium sand with black v.f. sand lenses (0-1”)
(mg/kg: ND<2.7 Hg /
21.5 As / 8.3 Pb)
23-32” BGS: Light gray coarse sand with black organic matter interbeds (<1”)
0”
2”
16”
23”
32”
8”

## Slide 25: Mercury concentrations for laboratory and XRF analyses of soil samples collected in upper FBC watershed
6/17/2019
FBC Data Summary Presentation

## Slide 26: Arsenic concentrations for laboratory and XRF analyses of soil samples collected in upper FBC watershed
6/17/2019
FBC Data Summary Presentation

## Slide 27: Lead concentrations for laboratory and XRF analyses of soil samples collected in upper FBC watershed
6/17/2019
FBC Data Summary Presentation

## Slide 28: Mercury and arsenic concentrations for XRF and laboratory splits of soil samples collected in upper FBC watershed
6/17/2019
FBC Data Summary Presentation

## Slide 29: Mercury and lead concentrations for XRF and laboratory splits of soil samples collected in upper FBC watershed
6/17/2019

## Slide 30: Sample Split Lab vs XRF Total Concentrations
6/17/2019
FBC Data Summary Presentation

## Slide 31: Results
Soil
  Presence of tailings/impacted soils are primarily limited to the riparian corridor and lower terraces of the floodplain (average width approximately 250 feet)
  Impacted material ranged between approximately 0 and 25 inches BGS
    Most impacts observed within the upper 12 to 15 inches
  Total mercury (Hg), arsenic (As) and lead (Pb) concentrations correlate strongly
  Mercury (Hg) and arsenic (As) are elevated, particularly in “tailings” layer
    Mercury ranged between below detection to 450 mg/kg
    Arsenic and lead ranged between below instrument detection and 17,100 mg/kg and 5,460, respectively
  Antimony concentrations (only 20 lab samples) were also elevated
    Antimony ranged between below detection to 530 mg/kg
  Soils and sands immediately beneath tailings/impacted soils and above groundwater in most locations had relatively low to below detection limits for mercury, arsenic and lead

## Slide 32: FBC floodplain cross-section schematic showing tailings, impacted, and non-impacted sediments and soils (not to scale).
6/17/2019
FBC Data Summary Presentation

## Slide 33: Typical sediment sample location on Fred Burr Creek

## Slide 34: Results
Sediment
  Mercury, arsenic and lead concentrations were comparable with values observed in the recent MDEQ sediment sampling
  Splits of the fine fraction (silt <63um) of samples had mercury, arsenic, lead and antimony concentrations between 2 to 3, 4 to 10, 4 to 6 and 2 to 6 times greater than bulk samples, respectively.
  Recent overbank flood deposits similar to sediment Hg and metal concentrations
    Implications for long-term impacts
COC | Bulk Sample Range (mg/kg) | Fine (<63um) Fraction Range (mg/kg)
Mercury | 8.6 - 21 | 25 - 64
Arsenic | 78 - 398 | 401 – 1,840
Lead | 36 - 132 | 172 - 572
Antimony | 4 - 19 | 11 - 78

## Slide 35: Recent (2017) flood overbank deposits on Fred Burr floodplain
Hg, As and Pb concentrations similar in overbank deposits and stream sediment

## Slide 36: Results
6/17/2019
FBC Data Summary Presentation
Surface Water
  Generally within the range observed in recent MDEQ sampling at similar locations
COC | Sample Range | MDEQ Aquatic Standard (chronic/acute) | MDEQ Human Health Standard
 | (ug/l) (lead @ hardness = 25 mg/l) |  | 
Mercury | 0.18 – 0.95 | 0.91/1.7 | 0.05
Arsenic | 13 - 25 | 150/340 | 10
Lead | 0.8 – 3.7 | 0.545/13.98 | 15
Antimony | 1.0 – 1.6 | NA/NA | 5.6

## Slide 37: Results
6/17/2019
FBC Data Summary Presentation
Groundwater
  Depth to GW ranged from 24-56” BGS in floodplain
  Analytical results are not conclusive, as groundwater was highly turbid at the time of sampling from piezometers

## Slide 38: Select Agency Soil Screening and Risk Levels
6/17/2019
FBC Data Summary Presentation
COC | Receptor (*) | Soil Concentration (mg/kg) |  |  |  | # and % sample locations with 1 or more samples > EPA removal criteria | # and % surface sample locations with 1 or more samples > EPA removal criteria | # and % of total samples > EPA removal criteria
 |  | BLM (1) | MDEQ (2) | EPA (3) | EPA (4) |  |  | 
Mercury | Residential | 2 | 1 | 11 | 33 | 27 (56%) | 24 (50%) | 52 (35%)
 | Rec/Commercial (*) | 40 |  | 46 | 140 | 17 (35%) | 10 (21%) | 23 (16%)
Arsenic | Residential | 3 | 40 | 0.68 | 68 | 40 (83%) | 39 (81%) | 94 (64%)
 | Rec/Commercial (*) | 20 |  | 3 | 300 | 39 (81 %) | 37 (77%) | 70 (48%)
Lead | Residential | 400 | 400 | 400 | 400 | 29 (60%) | 26 (54%) | 51 (35%)
 | Rec/Commercial (*) | 1000 |  | 800 | 800 | 21 (44%) | 17 (35%) | 34 (23%)
Antimony** | Residential | 1 | -- | 31 | 94 | 9 (45%) | 4 (20%) | 9 (45%)
 | Rec/Commercial (*) | 50 | -- | 470 | 1400 | 0 (0%) | 0 (0%) | 0 (0%)
* - BLM Receptor is for recreational camper; EPA receptor is industrial/commercial worker |  |  |  |  |  |  |  | 
(1) - Bureau of Land Management - Risk Management Criteria for Metals at BLM Mining Sites (Tech note 390 October 2004) |  |  |  |  |  |  |  | 
(2) - Montana Department of Environmental Quality - Tier 1 Risk Based Corrective Actions for Petroleum Releases (2009) |  |  |  |  |  |  |  | 
(3) - EPA - Regional Soil Screening Levels at Superfund Sites - Generic SSL's (November 2018); TR (carcinogenic)=1E-6;THQ (non-carcinogenic)=1 |  |  |  |  |  |  |  | 
(4) - EPA - Regional Removal Management Levels - Generic Values (November 2018); TR (carcinogenic)=1E-4;THQ (non-carcinogenic)=3 |  |  |  |  |  |  |  | 

## Slide 39: Screening Levels
6/17/2019
FBC Data Summary Presentation
Sediment
  Mercury
    All samples exceeded EPA BTAG freshwater benchmarks (0.18 mg/kg)
  Arsenic
    All samples exceeded EPA BTAG freshwater benchmarks (1.8 mg/kg)
  Lead
    All samples exceeded EPA BTAG freshwater benchmarks (35.8 mg/kg)
  Antimony
    All samples exceeded EPA BTAG freshwater benchmarks (2 mg/kg)

## Slide 40: Screening/Regulatory Levels
6/17/2019
FBC Data Summary Presentation
Surface Water
  Mercury
    All samples exceeded MDEQ human health standard
    A single sample exceeded MDEQ chronic aquatic standard
  Arsenic
    All samples exceeded MDEQ human health standard
  Lead
    All samples exceeded MDEQ chronic aquatic standard

## Slide 41: Conceptual Site Model schematic for potential tailings impacts and exposure pathways in the FBC floodplain.
6/17/2019
FBC Data Summary Presentation
?
?

## Slide 42: Contaminant Transport/ Exposure Pathways
Streambank erosion and fluvial processes
  Likely substantial source of elevated Hg and metals in sediment and SW
Groundwater
  Large decrease (2 orders of magnitude) in Hg and metal concentrations in underlying soil/seds Suggests limited movement via infiltration to GW
Floodplain surface runoff is likely minimal
  Floodplain has a low slope
  Floodplain also well-vegetated, minimizing runoff/erosion
Exposure due to ingestion or airborne soils likely minimal
  Well-vegetated floodplain
  Roads near mill site unknown
Mill site characteristics are the primary unknowns
  How much source material remains and where is it located?
  What does runoff regime look like?
  What is extent/degree of impacts in FBC floodplain near mill site?
    Effect of disturbance on distribution
    Road material contamination

## Slide 43: Contaminant Transport/ Exposure Pathways

## Slide 44: Soil (A) slumping into FBC channel as a result of streambank erosion and undercutting near SP-37. Also note red top and willows on top of the river bank—the vegetation assemblage observed with tailings impacts in the FBC floodplain.
6/17/2019
FBC Data Summary Presentation
A

## Slide 45: Next Steps What We Are Doing Now
  Develop volume estimate of tailings/impacted soils in floodplain using LiDAR, GIS and existing analytical data
  Sample domestic wells for Hg and metals
  Analyze sediments/soils for methylmercury
  Begin Preliminary Risk Assessment
  Refine Hg/metal source loading to FBC
    Estimate bank migration rates and develop estimate of sediment input and Hg/metal loading to FBC
    If warranted, install a few shallow monitoring wells to characterize floodplain GW quality