## Slide 1: Tree Response to Soil Treatments on Quarry Overburden
J.A. Franklin and D.S. Buckley
Dept. of Forestry, Wildlife and Fisheries
University of Tennessee
Presented at ASMR, June 6, 2019
Big Sky, MT

## Slide 2: Forestry Reclamation Approach
1. Create a suitable rooting medium for good tree growth that is no less than 4 feet deep and comprised of topsoil, weathered sandstone, and/or the best available material
2. Loosely grade the topsoil or topsoil substitutes established in step one to create a non-compacted growth medium
3. Use ground covers that are compatible with growing trees
4. Plant two types of trees – 1) early succession species for wildlife and soil stability, and 2) commercially valuable crop trees
5. Use proper tree planting techniques

## Slide 3: Forestry Reclamation Approach
Recommends seeding tree-compatible ground cover, and creating soil conditions that promote the establishment of trees and native vegetation.

## Slide 4: Forestry Reclamation Approach
Aggregate industry in 2019 (USGS):
$8.7 billion in construction products
$6.2 billion in industrial products
9,350 active quarries in US
Concentrated in populated areas
Tested extensively on reclaimed coal mines in the eastern US for establishing forest.

## Slide 5
Challenges in applying the FRA in different situations:
Differences in soil pH, soil texture, available nutrients
Fertilization effects
Lime application effects
coal mine quarry

## Slide 6: Project objectives:
Demonstrate the use of the FRA for the reclamation of quarry overburden
Test the influence of reclamation treatments on the establishment of planted trees:
Treatments:
Grading
Fertilization
Lime application

## Slide 7
Study site: Roger’s Quarry, Oak Ridge, TN

## Slide 8
Site construction: 2007-2008
Pre-disturbance
Valley filled with overburden
Compacted base
Feb. ‘09
Plot placement Mar. ‘09
Ready for planting May ‘09

## Slide 9: Soil properties
P 0.4 %
K 54.2 ppm
Ca 3626
Mg 1854
Zn 17.3
Cu 0.4
Fe 3.7
Mn 29.5
Na 18.7
N BDL
pH 5.1-5.6
66% > 2mm
26% sand
2% silt
6% clay
0.7% organic

## Slide 10
(46.78 L/Ha)
400 Kg/Ha N from 20:20:20
100 Kg/Ha N from 20:20:20
Graded
Un-graded
3 blocks, based on shading from adjacent forest

## Slide 11: Trees were planted 1 species per sub-plot
white oak shortleaf pine American Chestnut
(Quercus alba) (Pinus echinata) (Castanea dentata)
No ground cover was seeded

## Slide 12: Measurements
Soil pH of each plot was tested two times per year in 2009, 2010, and 2011. After 1 year there was no longer an effect of lime on pH, and it was re-applied in May 2010.
Soil temperature and soil moisture at 15 mm depth were measured twice per month during the 2009, 2010 and 2011 growing seasons.
Tree height and root collar diameter (RCD) were measured in May 2009, Dec. 2009, and during the summers of 2011, 2014, and 2016.
On un-graded plots, topographic position of each tree was noted.
Chart: soil pH
| 39873 | 39995 | 40269 | 40330 | 40360 | 40756
no lime | 5.33 | 4.6908 | 4.9328 | 4.9325 | 5.3367 | 4.7
lime | 5.33 | 4.9361 | 5.015 | 5.0758 | 5.4967 | 4.72

## Slide 13: 2013

## Slide 14: 2016

## Slide 15: 2016

## Slide 16: Results Main effects - fertilizer
Chart: Mean height (cm)
| Initial | Dec. 2009 | 2010 | 2011 | 2014 | 2016
Chestnut100 | 86.1 | 96.5333 | 118.625 | 145.6696 | 154.94 | 153
Chestnut400 | 88.475 | 100.1917 | 137.9917 | 193.1351 | 236.22 | 230
Oak100 | 28.15 | 33.0083 | 38.2833 | 41.827 | 55.88 | 61
Oak400 | 27.6417 | 33.6 | 40.075 | 54.9703 | 88.9 | 93
Pine100 | 23.725 | 26.5 | 34.9667 | 62.6202 | 119.38 | 175
Pine400 | 24.9917 | 29.1 | 40.7 | 93.2801 | 203.2 | 276
Chart: Mean RCD (mm)
| Initial | Dec. 2009 | 2010 | 2011 | 2014 | 2016
Chestnut100 | 10.4517 | 10.475 | 14.03 | 26.7063 | 33.7333 | 34
Chestnut400 | 10.8308 | 12.8333 | 17.6092 | 37.0844 | 54.8667 | 46
Oak100 | 6.2408 | 6.4 | 7.9292 | 13.0113 | 18.4333 | 20
Oak400 | 5.6975 | 7.1 | 8.3892 | 16.2593 | 25.5833 | 27
Pine100 | 3.87 | 4.8583 | 8.2017 | 24.3493 | 45.3 | 61
Pine400 | 3.6258 | 5.725 | 10.6167 | 30.5378 | 59.4917 | 78
*
*
*
*indicates a significant effect of treatment for the species at p> 0.05
*
*
*

## Slide 17: Results Main effects - fertilizer
*
*indicates a significant effect of treatment for the species at p> 0.05
Chart: % Survival
| 39904 | 40148 | 2010 | 2011 | 2014 | 2016
ches100 | 100 | 96.77 | 88.96 | 92.4 | 86.15 | 67.71
ches400 | 100 | 93.13 | 85.21 | 88.75 | 85 | 66.46
oak100 | 100 | 98.4028 | 92.2222 | 93.6806 | 87.5 | 87.5
oak400 | 100 | 97.6273 | 93.9815 | 95.3704 | 91.2616 | 88.8889
pine100 | 100 | 68.54 | 69.06 | 74.79 | 77.92 | 76.9097
pine400 | 100 | 61.88 | 58.23 | 67.19 | 64.9 | 60.4545

## Slide 18: Results Main effects – lime application
*
*indicates a significant effect of treatment for the species at p> 0.05
No effect on growth
Chart: % Survival
| 39904 | 40148 | 2010 | 2011 | 2014 | 2016
chestnutNL | 100 | 95.21 | 86.35 | 88.23 | 87.71 | 69.48
chesnutL | 100 | 94.69 | 87.81 | 92.92 | 83.44 | 64.69
oakNL | 100 | 96.956 | 91.2963 | 92.6968 | 85.5324 | 83.5648
oakL | 100 | 99.0741 | 94.9074 | 96.3542 | 93.2292 | 93.1818
pineNL | 100 | 71.67 | 68.54 | 76.15 | 76.56 | 75.0347
pineL | 100 | 58.75 | 58.75 | 65.83 | 66.25 | 62.5
*

## Slide 19: Results Main effects – grading
*indicates a significant effect of treatment for the species at p> 0.05
Mean volumetric soil moisture was significantly greater (16.06 % ± 0.37 SE) in graded plots than in ungraded plots with mounds (15.25 ± 0.41 SE).
*
Chart: % Survival
| 39904 | 40148 | 2010 | 2011 | 2014 | 2016
chestnutUG | 100 | 91.46 | 86.67 | 95.21 | 91.46 | 71.15
chestnutG | 100 | 98.44 | 87.5 | 85.94 | 79.69 | 63.02
oakUG | 100 | 97.1065 | 94.0856 | 97.4537 | 93.9699 | 91.8434
oakG | 100 | 98.9236 | 92.1181 | 91.5972 | 84.7917 | 84.7917
pineUG | 100 | 68.13 | 67.08 | 81.77 | 84.69 | 80.3409
pineG | 100 | 62.29 | 60.21 | 60.21 | 58.13 | 58.6806

## Slide 20: Results Influence of microtopography - aspect
Chart: RCD in 2016 (mm)
| Chestnut | Oak | Pine
N | 37 | 23 | 61
E | 41 | 22 | 63
S | 40 | 25 | 70
W | 44 | 28 | 63
Chart: Mean soil temperature (degrees C)
| N | W | E | S | T
 | 21.6761 | 22.0946 | 22.1509 | 22.3104 | 22.6764
C
B
B
B
A
No clear pattern for soil moisture

## Slide 21: Results Influence of microtopography – slope position
Chart: Height in 2016 (cm)
| Chestnut | Oak | Pine
Lower | 186 | 72 | 234
Mid | 204 | 88 | 219
Upper | 203 | 76 | 181
Chart: RCD in 2016 (mm)
| Chestnut | Oak | Pine
Lower | 37 | 22 | 71
Mid | 39 | 25 | 69
Upper | 42 | 24 | 58
*
Temperature – hotter on top
Soil moisture – no pattern
Organic matter – lower on top
Fertilizer – likely lower on top
Competition – lower on top

## Slide 22: Results Influence of microtopography
North
Mean RCD in 2019
Species did not differ in response, combined for analysis of 2016 data.
Clear gradient on northern aspect, not on southern.
Mid-slope position had more consistent growth.

## Slide 23
Conclusions
FRA techniques applied to quarry restoration resulted in successful tree establishment, similar to results seen on reclaimed coal mines.
Site preparation and soil amendments at the time of stand establishment can have a significant influence on tree survival and long-lasting effects on tree growth.
Microtopography has an influence on tree growth.

## Slide 24: Acknowledgements
Richard Evans and Kevin Hoyt, UT-FRREC
Roger’s Group – funding and site prep
UTIA and USDA McIntire-Stennis – funding
USFS and ACF – Chestnut seedlings
Technical assistance: Beth Aubuchon, Adam Klobucar, Aju Sahadevan, Veronica de Lima Neibles, Joslyn Knox, Brien Ostby