## Slide 1: Land Application Disposal System Design for Biochemical Reactor Treated Effluent
June 6, 2019
American Society of Mining and Reclamation Conference
N.R. Anton
D.T. Shanight
C.S. Storrar
M.J. Fischer
E.M. Janoviak
B. Lala

## Slide 2: Outline
Tenmile Site Background
Luttrell Repository Components
Pre-Design Investigation Activities
Full-Scale Passive Treatment Design Overview
LAD Design and Operation

## Slide 3: General Site Background
Location: Upper Tenmile Creek Mining Area Superfund Site
Contaminants of Concern: Al, As, Cd, Cu, Fe, Pb, Mn, and Zn
Currently addressing priority abandoned mine sites
  28 remediated to date (after 2015)
  54 mine sites remaining
Waste from contaminated residential yards and abandoned mines moved to Luttrell Repository

## Slide 4: Luttrell Repository
Regional repository
Former Basin Creek Mine – Luttrell Mine Pit
Serves Tenmile Creek, Basin Creek Superfund sites, and other high priority mine cleanups
Long-term leachate treatment approach

## Slide 5: Luttrell Components
Luttrell Repository
  Full liner system with leachate collection and treatment
  ~1 million CY capacity
Leachate Collection Pond
  ~750,000 gal capacity
Water Treatment Plant
  Up to ~50 gpm
BCR Pilot
Existing Land application disposal (LAD) system
Leachate Collection Pond
Winter Cover
BCR Pilot Pond
2015 Waste Placement Area
Water Treatment Plant
Storm Water Pond
LAD area

## Slide 6: Leachate Water Treatment Systems
Active Treatment Plant
Pilot BCR
Active conventional water treatment plant using sodium hydroxide
Pilot BCR - sulfate reducing bacteria (SRB) to reduce sulfate to sulfide and form metal sulfide precipitates
Systems are aging and require diesel generator power - long-term treatment solution needed
Existing Leachate pond undersized to accommodate spring melt

## Slide 7: Pilot-scale Biochemical Reactor
Startup in 2003
Operated through 2017 season
Design parameters:
  Max influent flow rate: 6 gpm
  Sulfate reduction rate: 300 mmol/m3-day
  Retention-time: 5.4 days
Substrate: straw, manure, wood chips, coarse limestone gravel
Adequate metal removal - Can use same sizing principles for scale-up system

## Slide 8: Land Application Disposal System
Existing System
  Diesel generator and pump operated from WTP and BCR
  Two LAD areas covering 16.7 acres
  ~2 acres of wetted surface area
  Site-specific discharge standards based on soil adsorption capacity
  Not ideal location for long-term application of treated water

## Slide 9: Land Application Disposal System
LAD benefits
  Avoids direct surface water discharge and required standards
  Utilizes sorption capacity of soils to remove residual metals and ions
  Provides supplement watering of forest or other type of ecosystem
  Site-specific sorption-based standards and/or GW-based standards
  Can be gravity operated for passive systems
LAD challenges
  Requires regulatory approval and coordination
  Could mimic or trigger ‘groundwater injection’ regulations
  Requires careful soil evaluation of proposed LAD area to ensure:
    Effective water retention
    Adequate sorption capacity
    Safe distance from wetland areas and near-surface groundwater

## Slide 10: Pre-Design Field Investigation
LAD field assessment
  Evaluate evapotranspiration and permeability of area soils using USDA and Montana resources
  Identify overall LAD areas
  Test pits in new potential LAD areas
  Lithologic logging
  Forest and wetland evaluation
  Soil analysis
    Total metals
    Agronomic properties
    Grain size analysis
    Remolded permeability
    Sand cone field density
    Metal sorption capacity testing

## Slide 11: LAD Soil Metal Sorption Study
Soil from 2 test pits in new potential LAD areas, A and B horizons
7 ratios of stock BCR effluent water to spiked BCR effluent water
  (10%, 5%, 2.5%, 1%, 0.5%, 0.2%, 0.1%)
  Spiked BCR effluent (As2O5, CdCl2, CuCl2, PbCl2, ZnCl2)
  Post-treatment aeration simulated
28 batch tests plus 2 replicates
Batch tests tumbled for 24 hours
Samples analyzed for metals analyses
  Subsample of soil from each location
  Stock BCR effluent water
  Batch tests

## Slide 12: LAD Soil Metal Sorption Study
LAD system metal sorption capacity
  Plotted data for each metal and sample
  Langmuir isotherm linear regressions to calculate sorption capacity
Soil Location | Source | Sorption Capacity (Qm) (mg/kg) |  |  |  |  | 
 |  | Arsenic | Cadmium | Copper | Lead | Manganese | Zinc
T4A | Calculated1 | 28.33 | 15.92 | 61.35 | 28.01 | 48.54 | 285.71
 | Estimated2 | 28.8 | 5 | 45 | 40 | N/A | 250
T4B | Calculated | 1.12 | 2.18 | N/A | 34.72 | N/A | 212.77
 | Estimated | 1.2 | 10 | 18 | 40 | N/A | 200
T7A | Calculated | 8.10 | 1.80 | 27.10 | 26.88 | N/A | 69.44
 | Estimated | 8.1 | 1.2 | 30 | 35 | N/A | 65
T7B | Calculated | 20.92 | 0.84 | 31.15 | 97.09 | 36.50 | 80.65
 | Estimated | 2.1 | 0.8 | 30 | 100 | N/A | 90
Chart: T7A, Copper Adsorption Test- Langmuir
| 0.74099999999999999 | 0.314 | 0.188 | 9.8599999999999993E-2 | 6.6000000000000003E-2 | 7.2800000000000004E-2 | 6.7000000000000004E-2
 | 0.029754 | 0.015607 | 0.011212 | 0.0066213 | 0.0046172 | 0.0053246 | 0.0049462

## Slide 13: LAD Area Sorption Capacity
Mass of each metal over operational period
  92-day treatment season x 12.5 gpm = 1.6 Mgal
  Average 2015 effluent metals concentrations
Volume of soil in proposed LAD area
  6.3 acres x 8 ft = 62,000 m3
Use sorption capacity from tests
Calculate sorption life in years
Lifespan = 22 years (conservative)
  Partial removal Mn in post-treatment
  Fluctuation of Mn concentrations year to year
  Precipitation of Mn-oxides (rather than sorption)

## Slide 14: Pre-Design Field Investigation
Leachate pond stability evaluation
  Hollow-stem auger drilling at existing pond areas
  Geotechnical properties
  Inclinometer installation to evaluate embankment movement
  Geotechnical calculations
Area fill evaluation
  Excavation of test pits in proposed construction areas
  Identification of available fill/excavation depths
  Estimation of oversize rock content
Existing Fill Slope
~60 feet high
Expanded Leachate Pond
Boring Locations

## Slide 15: Full-Scale Passive Treatment Design Overview
Leachate collection pond
  1.8 Mil gallon - built in current pilot BCR and stormwater pond area
  Pre-treatment oxidation – windmill powered aerator
  Size based on maximum runoff, direct precipitation inflows, leachate inflows, and repository construction inflows
    Treatment only
    July – September
New Stormwater Pond
  Unlined
  Built in existing leachate pond area – smaller capacity

## Slide 16: Full-Scale Passive Treatment Design Overview
Leachate transfer
  ~1300 feet long, gravity flow
  6-inch HDPE primary, 3-inch HDPE backup
  Cleanouts ~ every 300 ft
  Flow control vault and splitter basin to BCRs
    V-notch stainless flow control valve
    Mag flow meter
    Concrete splitter basin to
    send equal flow to each BCR

## Slide 17: Full-Scale Passive Treatment Design Overview
Biochemical Reactor
  12.5 GPM design flow based on water volume and treatment season
  Two parallel BCRs 2X design flow (25 GPM)
  Down-flow
  Limited surficial piping (flooded)
  3 effluent perf pipe zones with isolation valves
  Cleanouts on each lateral
  Level control structure
    Allows drain to substrate top surface for winterization
    Freeze insulated vault

## Slide 18: Full-Scale Passive Treatment Design Overview
Post-treatment
  Anaerobic settling pond
    Quiescent settling of organic matter and sulfides
    Minimizes metal sulfide oxidation
    Drop structure/aeration at outfall
  Limestone-lined aeration channel and cascades
    Provides alkalinity and aeration/oxidation
    Manganese removal and
    additional trace metal polishing
  Aerobic settling pond
    Windmill-powered aerator
    Outlet to LAD pipeline
    ~300 ft long, 3-inch HDPE

## Slide 19: Full-Scale LAD Design Basis
No power available – no pumping
Low available head
  Current LAD sprinkler approach would not function
Need even flow distribution
24/7 unattended operation
Notes: Unattended operation, meaning it has to function by itself and so not able to use a large (10,000+ gal) holding tank that is drained periodically like the current system.

## Slide 20: Full-Scale LAD Design Basis
Dosing Siphons
  Dosing siphons provide high flow rate to pressurize system
  Gravity flow system
Design Flow
  Flowrates determined by siphon size
  Design = 4” Siphon = 170 gpm flowrate
Copyright 2013 ©Fluid Dynamic Siphons, Inc.
Siphons.com
Notes: For the dosing siphon, we can talk about the fact that we can’t just run 12.5 gpm out to the LAD because basically only the last few holes in the pipe would be flowing and it would overload that section of the LAD soils

## Slide 21: Full-Scale LAD Sizing
Distribution area determined by soil infiltration rate – no runoff
Soil Infiltration Rate (e.g., percolation rate)
  Remolded permeability measurements using sand-cone field density
  Assumed 20% of permeability was available for infiltration
    Calculated available hydraulic loading rate for the soils
Calculated required LAD area based on hydraulic loading rate
LAD size ~ 1 acre for 12.5 GPM

## Slide 22: Full-Scale LAD Sizing
Design flow: 170 gpm) LAD area too large when calculated using hydraulic loading – 14 acres!
  Calculation assumes continuous flow and not pulsed flow – Not Correct
Design check - assume pulsed flow is rainfall and use curve number hydrologic calculation method
  CN = 70 (Woods, Good Condition, HSG – C)
  Set volume of pulse equal to initial abstraction for no runoff
  Back calculate required area to absorb dose volume
  0.11 acre required area – much smaller than available area to account for antecedent moisture
Final design LAD area = 6.25 acres
  More than adequate space available based on hydraulic loading
Notes: Also checked the required area for 12.5 gpm and 25 gpm continuous flowrates using the SCS CN method. Results compared favorably to the method using permeability and hydraulic loading rate

## Slide 23: Full-Scale LAD Design Overview
Dosing Siphon and Tank Design
  Commonly used in septic drainfields
  Perforated pipelines distribute flow
  Distributes flow into the entire piping system and receiving soil
  Dual siphons in one tank provide flow to two LAD zones
Hydraulics
  4 individual LAD zones with isolation valves
  4 Perforated pipelines within each zone laid on contour – 16 pipelines
  Available head for each pipe determined
  Orifice size and spacing calculated based on pressure and flowrates in each lateral

## Slide 24: Full-Scale LAD Design Overview
Notes: Valves on laterals will allow for adjustments to ensure even flow distribution once system is operational. Calculations and real-world sometimes don’t match up.

## Slide 25: Full-Scale LAD Design Overview
Siphon Operation Parameters
  1,500 gallon dose volume
  ~10 minute dose time
  2 hour fill time between doses (12.5 gpm fill rate – 1 BCR)
  Dual siphons – 4 hours between doses to a single LAD zone
  Available head 7 – 22 feet
  Valving will allow adjustments to laterals as necessary
  Can isolate one zone or use all zones, and portions of laterals within each zone

## Slide 26: Questions