## Slide 1: Successful Erosion Control and Revegetation Techniques for Mine Reclamation & Revegetation
Presented by:
Brent Hardy, MS, CPESC

## Slide 2: Our Challenges to Start….
Low annual precipitation
Long hot summers
Rocky soils with low organic matter
Potentially high background levels of salts and metals
Notes: Over worked soils/cooked stockpiles, low biological activity, loss of soil structure, low nutrients, high or low pH, possibly elevated metals.

## Slide 3
Pulverize our soils destroying soil structure, reducing biological activity, and organic matter
Construct steep slopes
Compact soils with heavy equipment
And then we…

## Slide 4: Reclamation Strategies for Success
Step 1: Understanding Your Onsite and Imported Soils
Step 2: Erosion Control: Keeping Soils Where They Belong
Step 3: Establishing & Maintaining Long-Term Vegetation
Notes: Mention that we have an outside free soil testing for the basic NPK and OM

## Slide 5: Step 1: Understanding You’re Soils

## Slide 6: Soil Testing
Conduct representative soil tests in each unique landscape area to determine:
  Soil pH
  Fertility requirements/deficiencies
  Organic matter content
  Specific site conditions (e.g. metals, salts, pollutants)
Design your revegetation plan based on the results
Notes: Mention that we have an outside free soil testing for the basic NPK and OM

## Slide 7: How Does pH Effect Plant Establishment?
pH is second only to moisture availability in immediate impact on vegetation establishment
Each unit is 10 times that of the previous or next unit
Minor movements in pH can serious impact nutrient availability or toxic metal mobility
Notes: Add that pH is easily adjustable in either direction and inexpensive

## Slide 8
Soil Acidity Nutrient Loss
4.0 pH - 90%
4.5 pH - 71%
5.0 pH - 54%
5.5 pH - 33%
6.0 pH - 20%
↓ 6.3 pH - 0% ↓
↑ 7.3 pH - 0% ↑
8.0 pH - 20%
8.5 pH - 33%
9.0 pH - 54%
9.5 pH - 71%
10.0 pH - 90%
Soil Alkalinity Nutrient Loss
pH
Sweet Spot
Nutrient Uptake

## Slide 9: Handling of Soils Plays a Critical Role in Successful Restoration
Notes: The first step involves understanding your soils, where they came from (direct-haul or stock-piled), and how much you have is only the beginning.

## Slide 10: Stockpiling of soils will reduce most of the living components of the soils
~30 ft tall
8.8 acre footprint
Notes: Decreases OM, soil structure, and biological activity

## Slide 11: Soil Foodweb – Key to Healthy Soil
Mycorrhizae increases nutrient availability for plant uptake
Nitrogen fixing bacteria will cycle existing nutrients in soils
Builds soil structure & cycles organic matter

## Slide 12: Soil Mycorrhizae
A fungus that aids in the absorption of nutrients by forming a symbiotic relationship with plant roots
90% of plants form a relationship with mycorrhizae
They dramatically increase the absorptive area of root systems
Reintroduction of mycorrhizae can dramatically improve plant performance with less water and fertilizer
Notes: Current, as of 3/23/16.

## Slide 13
Equipment Selection: Choose Wisely
Think about soil compaction
Weight differences of a wide-track D6T (21-tons) vs a D10T (73-tons)
Notes: The weight differences between a D10 (foreground) vs a wide-track D6 is significant, so less pounds per square inch will help considerably in minimizing compaction.

## Slide 14: Step 2: Erosion Control: Keeping Soils Where They Belong
Notes: Add photo

## Slide 15: Erosion Control
Track walking to increase roughness
Straw or excelsior wattles following slope contours to break up slope
Erosion control blankets
Hydromulching
Notes: Mention importance of longevity, time of year, precip, etc

## Slide 16
Do It Right the First Time!

## Slide 17: Install Wattles on the Contour

## Slide 18: Hydromulching
Provides more uniform coverage, better soil contact, and increased moisture retention
Allows mixing of seed, fertilizer, amendments in one load
Adaptable to site conditions
  Slopes
  Soil types
  Number of growing seasons estimated for plant establishment
Quick coverage over large acreages

## Slide 19: After Three Weeks of Growth
Dual Application Process

## Slide 20: Dry application when there is a lack of water, long slopes, equipment limitations, or tight material specifications on cap & cover systems.

## Slide 21: Turf Reinforcement Mats (TRMs)
Permanent Plastic Growth Medium
  Roots and shoots grow through the mat and increases soil surface stability
Can be used with channelized flows
Anchoring systems can be incorporated to address shallow plane failure or allow near vertical installations

## Slide 23: Step 3: Establishing & Maintaining Long-Term Vegetation

## Slide 24: Seed Selection
BE REALISTIC!!!
Grow plants designed for the site conditions, consider:
  Soil type
  Annual precipitation
  Elevation and aspect
  Time for seed to break dormancy
Established or required mixes from agency or bond holder
Locally or site collected seed materials
Mixes/species with established track records

## Slide 25: Preserving Existing Vegetation is Your Fastest and Easiest Approach

## Slide 26: Using a Diverse Seed Mix Will Provide the Best Results
Nurse Crop

## Slide 27
The Beauty of a
Diverse Seed Mix
Notes: At Monsanto, we believe in having a very diverse seed mix to reclaim the mine land to it’s natural or better condition. The environmental regulations say that we need about 8 different grasses in our seed mix. However, we have 15 and 19 different grasses and forbs in our seed mixes, and most of those are native plant species.

## Slide 28: There’s help and its free…
Technical Notes from USDA Plant Material Centers
State and Federal agencies
Seed Produces and Vendors

## Slide 29: Re-establishing Native Shrubs and Trees
Notes: Besides the diverse seed mixes, we also plant several thousand native trees and shrubs each year on the reclaimed areas at the mine. Quaking aspen, lodge pole pine, and bitterbrush are the common species planted each year.

## Slide 30: Successful Reclamation
Reclamation is more than planting grasses and trees. Successful restoration, involves restoring systems, such as providing habitat and cover for wildlife.

## Slide 31: Lessons Learned – The Good and the Bad

## Slide 32: Vernal, Utah – When You Do Everything Right and it Still Goes Wrong
Took soil samples
Designed a soil amendment and cover program
Designed a seed mix that fit the draughty soil conditions and high salt contents
Applied everything correctly
What Happened!

## Slide 33: Importing Soil with Weed Seeds
Placed soil full of cheat grass (Downy Brome) seed, that exploded when fertilized as part of hydroseeding operation
Yellow Sweet Clover thriving in an area without surface soil importing

## Slide 34: Blackfoot Bridge Mine Soda Springs, ID
23,650 linear feet (4.5 miles) of Excelsior wattles installed on 5-ft contour intervals.

## Slide 35: Erosion Controls Correctly Placed
Slope length was 600+ feet on a 3:1 east-facing slope.
Oct 2014

## Slide 36
June 2016

## Slide 37
June 2016

## Slide 38
Nov 2016

## Slide 39: THANK YOU!! & QUESTIONS?
Brent Hardy, MS, CPESC
208-863-7529
Brent.Hardy@acfwest.com